Publish in JINST

Aims

We should make the paper of interest for non-ATLAS readers so that they can learn what we did and understand for themselves how to undertake comparable projects.

We should avoid discussing tedious detail for the sake of it – ultimately the design is documented by drawings stored on CDD and EDMS documents.

Schedule

Vsn 4 (mid Sep)

- First Draft for SCT Collaboration

- Author lists (see JINST instructions)

Vsn 5 (mid Oct)

- Revised draft, taking in comments. Include Author list.

- Second Draft for SCT Collaboration

Vsn 6 (end Oct)

- Final version

- Extract pictures

- Submit to JINST – must be before release of ATLAS Detector Paper on 1 Dec

Contributors

- Pawel Bruckman

- Craig Buttar

- Paul Dervan

- Didier Ferrere

- Peter Ford

- Martin Gibson

- Stephen Haywood

- Nigel Hessey

- Tim Jones

- Caroline Magrath

- Chris Nelson

- Brian Smith

- Luis Sospedra

- Jason Tarrant

- Tony Weidberg

- Patrick Werneke

- Ian Wilmut

1.	Introduction	6

1.1	Overview of the ATLAS Inner Detector	6

1.2	Overview of the SCT End-caps	7

1.3	Requirements	8

1.4	Introduction to Interfaces	9

1.5	Overview of the Cooling	9

2.	Disks	10

2.1	Bare Disks	10

2.1.1	Design	10

2.1.2	Choice of Korex®	11

2.1.3	Manufacture	11

2.1.4	Quality Control	13

2.1.5	Properties of the Disks	14

2.2	Services	14

2.2.1	Cooling Circuits	15

2.2.2	Other Services	18

2.2.3	Services Assembly and Testing	21

3.	Module Mounting	23

3.1	Module Mounting	23

3.2	Testing	26

4.	Support Structures	28

4.1	Design	28

4.1.1	Support Cylinder	29

4.1.2	Front and Rear Supports	30

4.1.3	Support Mechanisms	31

4.1.4	ITE Cylinder	32

4.1.5	FEA	32

4.2	Manufacture and Testing	33

5.	Cylinder Services	34

5.1	Evaporative Cooling Interconnects	35

5.2	Low-mass Tapes	35

5.3	Remaining Services	36

6.	End-cap Assembly	37

6.1	Support of the End-caps	37

6.2	Disk Insertion	38

6.3	Services Assembly	40

6.4	Testing during Macro-Assembly	41

7.	Transportation of the End-caps	41

7.1	Requirements	41

7.2	Designs of the Transportation Boxes	42

7.3	Transportation	43

8.	Thermal Enclosures	43

8.1	Requirements	43

8.2	Design Overview	44

8.3	Prototyping	45

8.3.1	Glue Applications	45

8.3.2	Small Cylinders	45

8.4	Design and Manufacture	46

8.4.1	OTE	46

8.4.2	Rear Thermal Pad	47

8.4.3	ITE	47

8.4.4	Heater Pads	47

8.4.5	Membranes	48

8.4.6	FEA Studies	49

9.	Final Assembly and TRT Integration	50

9.1	Final Assembly of the SCT	50

9.2	TRT Integration	52

9.3	Survey	54

9.4	Tests after Integration into the TRT	54

10.	Integration into ATLAS	55

10.1	Transport and Insertion into ATLAS	55

10.2	Installation of Services	56

11.	Grounding and Shielding	58

11.1	Concepts	58

11.2	Measurements	59

12.	Status of the End-caps	60

12.1	Status of the Hardware	60

12.2	Mass Estimates	60

12.3	Expected Tracking Performance	61

13.	Things To Do Differently	61

13.1	Layout	61

13.2	Disk Services	62

13.3	Large Structures	63

13.4	Assembly	63

14.	Conclusions	63

15.	Acknowledgements	63

16.	References	63

Engineering for the ATLAS Semiconductor Tracker

Abstract

The ATLAS Semiconductor Tracker (SCT) is a silicon-strip tracking detector which forms part of the ATLAS Inner Detector. The SCT is designed to track charged particles produced in proton-proton collisions at the LHC at an energy of 14 TeV. The tracker is made up of a central Barrel and two identical End-caps. Each End-cap supports 988 silicon modules.

This paper describes the engineering design, prototyping, construction and testing required to support mechanically the silicon modules, supply services to them and provide a suitable environment within the Inner Detector. Important engineering choices are highlighted and innovative solutions are presented – these will be of interest to other builders of large-scale tracking detectors.

One End-cap (EC-C) was assembled in the United Kingdom by a collaboration of the universities of Glasgow, Lancaster, Liverpool, Manchester, Oxford, Sheffield and the Rutherford Appleton Laboratory (STFC); the second End-cap (EC-A) was assembled in the Netherlands by NIKHEF (Amsterdam).

Keywords: LHC, ATLAS, SCT HAYWOOD

Authors

ALL SCT Collaborators  HAYWOOD

The Technical Staff at key institutes will be thanked by Institute in – see Acknowledgements.

# Introduction

## Overview of the ATLAS Inner Detector

The ATLAS Inner Detector [1] is designed to track charged particles produced in proton-proton collisions at the LHC at an energy of 14 TeV. In doing so, it measures their momentum, direction and impact parameters as well as providing some particle identification using transition radiation. The detector is also necessary to resolve multiple vertices from the overlap of ~23 collisions expected at design luminosity and the measurement of secondary vertices.

The Inner Detector consists of the Pixel Detector with 80 million pixels at the innermost radii, a silicon strip detector (SemiConductor Tracker, SCT) with 6 million strips and outside these a Transition Radiation Tracker (TRT) which contains 400 000 straws for charged-particle tracking and transition radiation detection to distinguish between electrons and pions. The detector sits in a solenoid magnet [2] which provides at its centre a 2 T field. The Inner Detector is designed to provide precise tracking up to || = 2.5, where  is the pseudorapidity, defined in terms of the polar angle:  = ln(tan(/2)).

The SCT provides precise tracking without the cost and expense of the pixel detector. The SCT is instrumented with 2112 silicon modules in the Barrel and 988 modules in each of the two End-caps [3]. The modules typically consist of 4 silicon wafers, each of the order of 6 cm by 6 cm. Two wafers are bonded together to form strips which are effectively 12 cm long. The strips are 80 m in the Barrel and have a key-stone (radial geometry) in the End-caps, with widths around 80 m. The front and back pairs of wafers are rotated by 40 mrad with respect to each other to provide a stereo measurement. The effective precision obtained with a module is around 17 m in the transverse directions and 580 m along the strips [4].

The SCT consists of four instrumented cylinders in the central region and a set of nine instrumented disks in each End-cap. Modules are arranged on the disks so that a charged particle originating from the interaction region should cross at least four layers of SCT modules: the pseudorapidity coverage of the disks starts where the coverage of the cylinders finishes. By design, the two End-caps are intended to be identical. The layout of the Inner Detector is shown in Fig. 1.

Fig. 1. Layout of the ATLAS Inner Detector. The SCT End-cap is indicated by “Forward SCT”.

Note on coordinate systems: The z-axis is along the axis of the experiment (in the direction of the colliding beams). In the transverse plane, the x-axis is horizontal and the y-axis is vertical. Cylindrical coordinates (R,,z) are used and the most important measurements, denoted by R, are made in the transverse plane, normal to the radial direction.

## Overview of the SCT End-caps

Each disk has up to three rings of modules: outer, middle and inner. The modules in each ring overlap to avoid gaps in azimuth; the rings overlap in radius, as seen from the interaction region. The SCT is designed to be hermetic for charged particles of pT > 1 GeV, nevertheless, there are small gaps in the acceptance, in particular there are only three measurements made in a small transition region between the Barrel and each End-cap. The module sizes are designed to optimise the size of silicon detectors cut from wafers. This results in 52 modules being required for the outer rings, but only 40 modules for the middle and inner rings.

In each End-cap, the disks are numbered from 1 to 9, starting nearest the interaction region. It is not necessary for all disks to have all of outer, middle and inner rings of modules to ensure full coverage. The association of module rings with disks is indicated in Tab. 1, along with the position of the centre of the disk as measured from the nominal interaction point. The middle ring is rotated by half a module with respect to the inner ring to avoid the material associated with module cooling blocks lining up in azimuth.

|  | Disk number |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| Position (mm) | 835.8 | 934 | 1091.5 | 1299.9 | 1399.7 | 1711.4 | 2115.2 | 2505 | 2720.2 |
| Stereo (mrad) | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 20 |
| Outer | 52 | 52 | 52 | 52 | 52 | 52 | 52 | 52 | 52 |
| Middle | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 |  |
| Inner |  | 40 | 40 | 40 | 40 | 40 |  |  |  |

Tab. 1. Disk positions, stereo angles and the number of modules in each ring.

All the modules in a given ring are exactly the same; however to reduce correlations in the measured track parameters and minimise asymmetries, the orientation of the modules alternates: on Disk 1, all the modules are rotated by +20 mrad (clockwise, as viewed from the interaction point), so that the strips of the front layer of silicon are rotated by +40 mrad, while those of the second layer are radial [5]. On Disk 2, the rotations are reversed, so that the strips of the front layer of silicon are radial, while those of the second layer are rotated by 40 mrad. For Disk 9, which has modules only on one side, the disk is rotated back-to-front to maximise the rapidity coverage by placing the modules further from the interaction point. This requires that it is built with the same stereo rotations as the even-numbered disks, while the orientation encountered by charged tracks is as if it were an odd-numbered disk. The alternating stereo configurations is realised by rotating the blocks on which the modules are mounted by ±20 mrad from the radial direction for alternately numbered disks.

The disks are supported in a large support cylinder which in turn is held by panels at either end which attach to the TRT rails. The End-cap is surrounded by a light thermal enclosure which comprises an outer and an inner cylinder. The services supplying the modules run on the surface of the disks and along the support cylinder, exiting at the services thermal feed-through (STFT) and then running in cable trays until the leave the Inner Detector volume at the corner of the cryostat, which holds the solenoid and the electromagnetic calorimeter.

Connections to services are made at the hybrids which are incorporated in the modules, at the PPF0’s (forward patch panels) on the outer radius of the disks and at the PPF1’s at the end of the ATLAS solenoid.

## Requirements

The SCT is deigned to provide four space-point measurements for a particle originating from the interaction point with || ( 2.5.

Placement Precision: The modules are built with internal precisions O(10) m, and with a tolerance of 5 m in the most critical dimension in the transverse measurement direction [3]. They are capable of measuring space points to 17 m and so if the uncertainty in the position of the module is not to degrade the momentum resolution by more than 20%, the position must be understood to better than 12 m in the transverse direction. For precision electroweak measurements, precisions more like 1 m are desirable. To a large extent, the actual position of the modules can be determined with high precision O(1) m during operation from the off-line alignment using particle tracks. This reduces the need to achieve very precise placement of the modules and the support structures. Nevertheless, the better the placement, the more readily the alignment procedures will converge and the easier it will be to understand systematic uncertainties. The only significant requirements come from ensuring sufficient overlaps between modules to allow precise module-to-module alignment and minimise holes seen by particles coming from the interaction point. This requirement is most stringent in the transverse R direction and is easily achieved in the radial direction because of the overlaps built in to allow for the nominal 5.6 cm beam-spot variation along the axis. The placement tolerances are summarised in Tab. 2 [6].

| Placement of modules in R (see Section 2.2.3) |
| --- |
| Module type | Module placement (m) | Mounting pin location (m) |
| Inner | 67 | 37 |
| Middle | 90 | 60 |
| Outer | 220 | 190 |
| Placement of disks |
|  | x-y (m) | z (m) |
|  | 100 | 1000 |

Tab. 2. Placement tolerances. The difference between the module and mounting pin tolerances arises from the tolerances on the location of the mounting washer on the module.

Stability: If the module position can be established by internal alignment using charged tracks with a frequency of once per day, then 1 m/day stabilities are required. This may be difficult to achieve for large structures and so the inherent stability will be complemented by internal length measurements within the SCT, determined by a frequency scan interferometer (FSI) [7][8][9]. The FSI system will measure lengths to O(1) m precision several times per hour. Nevertheless, to reduce possible systematic displacements of modules, it is desirable to construct a detector so as to minimise distortions.

Thermal management: Modules after irradiation will produce up to 10 W each [3], resulting in 10 kW generated in each End-cap. Long-term irradiation will lead to increased noise and eventually thermal runaway. Therefore to minimise the effect of reverse annealing, it is desired to keep the silicon at oC. In the SCT, heat sources have been minimised and by design, the cooling system will extract heat at source so that, as far as possible, the SCT will be operated at a constant temperature. To minimise the effects of thermal variations in time or space, low coefficient of thermal expansion (CTE) materials have been used for the support structures.

Moisture management: The inside of the SCT will be flushed with dry nitrogen. Before the first data-taking, the SCT will be flushed for several weeks, which will be sufficient to remove most of the stored moisture. To minimise the effects of any out-gassing of water vapour, low coefficient of moisture expansion (CME) materials have been used for the support structures.

Environment: The SCT detectors will be surrounded by dry nitrogen at 0oC – it is important to exclude carbon-dioxide (the environmental gas of the TRT and Inner Detector), which in the presence of water vapour, can form carbonic acid which attacks silicon detectors. The lower temperature will reduce the radiation damage experienced by the detectors, in particular the effects of reverse-annealing [1].

Radiation: The materials used must be able to withstand hadron fluences of the order of 1014 cm2 neutron equivalent over a period of 10 years. To facilitate safe access to the detector during interventions, nuclear activation must be minimised [10]. Silver is particular troublesome, so local concentrations were kept to below ~1 g.

Electrical Shielding: It is important to minimise electrical noise seen by the SCT from external sources (other components of the Inner Detector or the interaction region) and the emission of electrical noise which might affect other detectors. This requires the SCT is shielded by a conductive layer connected to ground; any apertures in the shield should not be more than a few cm2.

Materials: All materials must satisfy CERN fire standards; dispensations are required for materials which don’t. Magnetic materials which would distort the measured solenoidal field should be avoided. Most magnetic material will saturate in the 2 T field with a magnetisation of 0Msat. The requirement is that the sum of 0Msat×Vol for all magnetic materials should not exceed 20 T(cm3.

Mass: To reduce the multiple scattering of charged particles, nuclear interactions, bremsstrahlung of electrons and photon conversions, material must be reduced and where possible, materials with longer radiation lengths should be used. Reducing the mass of components where possible allows the material in the supports to be reduced.

## Introduction to Interfaces

The SCT End-cap has a defined geometric envelope, but otherwise has no explicit connections to the SCT Barrel, the Pixels or the TRT. The SCT End-cap is supported by the same rails which support the TRT End-cap, which in turn are supported by rails fixed to the cryostat. The Pixel Detector and its services are held within a CFRP cylinder: the pixel support tube (PST). The PST is supported by the SCT Barrel in the central region and is connected to the Inner Detector End-plate at the ends.

The SCT has an internal environment of nitrogen, while the Inner Detector is surrounded by carbon dioxide. The silicon of the SCT Barrel is at a similar low temperature of 7oC, while the PST facing the inside of the SCT End-caps will be at around 0oC and the TRT will be around 22.5oC.

Originally, it was expected to have a set of TRT wheels behind the SCT End-caps, however these have been staged and for the start-up of ATLAS, this volume will be used by the SCT services. The major interaction between the SCT End-cap and the SCT Barrel and TRT is in the region along the Cryostat where all the services run together.

## Overview of the Cooling

SCT modules (and Pixel modules) are cooled by evaporating C3F8 liquid in cooling pipes which are in good thermal contact with the modules – the process is similar to that of a commercial refrigerator [11]. Liquid is supplied to the detector at around 0oC and 14 bar. Capillaries which terminate at the start of the on-disk cooling circuits allow the liquid to boil in the presence of a heat source, leading to a vapour temperature of around 25oC. By contrast with utilising the specific heat of the fluid, the temperature along the pipe is isothermal, with a small drop of ~2oC associated with a reduction in vapour pressure along the pipe.

To make the system more efficient, heat exchanges just outside the SCT bring the warm incoming liquid and the cold outgoing vapour into close contact. The system is passive in so far as there no regulation of the flow-rate of liquid. To ensure that all modules along the cooling circuit can be cooled, there must still be liquid coolant left at the cooling exhausts. However, to avoid cold fluid returning in the exhaust pipes and needing to be lagged to avoid the formation of frost on the exhaust pipes outside the Inner Detector environment, heaters beyond the SCT boil off the remaining liquid.

# Disks

## Bare Disks

The End-cap modules are supported on carbon-fibre reinforced plastic (CFRP) composite disks comprising two CFRP facesheets and a honeycomb core. These disks must also

- Support the module services – see Section 2.2.

- Supply mounting points by which the disks are held in the support cylinder.

- Allow handling of the disk, complete with modules, during assembly and integration into the support cylinder.

It is important that the disks are a thin as possible while retaining adequate stiffness. This is important to minimise the gaps which exist between the rings of modules on alternate sides of the disks as seen by tracks coming from a range of collision points within the beam-spot envelope (z = 5.6 cm).

The dimensional requirements are summarised in Section 2.1.1; other requirements include [12]:

- The changes induced in going from assembly conditions (+20oC and 50% RH) to running conditions (15oC and <2% RH) should be less than 250 m/m.

- In normal running conditions, dimensional changes in the plane of the disk induced by ±2oC and ±0.5% RH changes should be less than 10 m/m.

- The first natural frequency of the bare disk should be higher than 40 Hz and greater than 15 Hz for the fully assembled disk.

- The maximum displacement on the statically loaded disk should be less than 10 m in plane and less than 100 m out of plane.

- The electrical resistance across the disk should be less than 0.5 .

### Design

The bare disks were made of CFRP facesheets 200 m thick and 8.3 mm thick sheet of honeycomb core. The facesheets comprised three plies of high-modulus graphite fibres and cyanate-ester resin set at (60o to each other. The honeycomb core used was Korex® – a high-performance aramid/phenolic honeycomb core with a cell size of 5/32 inch. The disks were sealed with U-profile rings at the inner and outer radii. The dimensions are summarised in Tab. 3.

| Dimension | Value (mm) | Tolerance (mm) |
| --- | --- | --- |
| Inner radius | 276 | ±0.2 |
| Outer radius | 567 | ±0.2 |
| Concentricity | 0.3 |  |
| Thickness | 8.7 | ±0.2 |
| Flatness | 0.5 |  |

Tab. 3. Disk design dimensions.

### Choice of Korex®

Extensive studies were undertaken to choose an optimal core for the disks [13]. In particular, the relative merits of ultra-high-modules carbon-fibre (UCF) and Korex® were considered. Korex® is made of aramid fibres bonded with phenolic resins resulting in a material with reduced moisture absorption and hence better dimensional stability than its predecessor, Nomex®. It is important to create a composite capable of withstanding machining forces during manufacture as well as peel, sheer and tensile loadings during use. To compare different composites, the flatwise tensile strength (FWT) was measured. This is a measure of the force required to pull apart a panel laterally: ideally the failure should be in the core, not the glue layers.

The preferred glue is based on cyanate ester, since it has low water absorption, typically 0.5% by mass compared with 6% for epoxies. However, cyanate esters are very sensitive to water when curing, and since Korex® has a high water content on delivery, it was found necessary to dry the core before use.

The FWT’s for UCF cores with different glues and different preparations were quite variable: between 0.4 and 1.7 MPa, whereas 2.6 MPa was achieved for Korex ® with RS4 and 3.6 MPa for Nomex® with epoxy. The effects of shrinkage due to loss of moisture when in operation is expected to cause radial movements with Korex® of 70 microns for the middle modules (the ones with their mounting points at the highest radii) – this is much less than the tolerance of 200 m, and actually corresponds to an increase in overlap, and hence is not a problem. Since the stiffness depends on the complete composite, the Korex® composites were found to be comparable in stiffness to UCF, despite the lower shear modules of Korex®.

Because of the better bonding achieved with Korex® and the fact that it was 60% of the cost of a UCF core (a significant fraction of the total cost), Korex® was chosen for use in the disks and, to ensure consistent physical properties throughout the End-cap, it was also used for the support structure.

### Manufacture

The disks were manufactured in an autoclave by Programmed Composites Inc (PCI). The main difficulty was in keeping the flatness tolerance of 0.5 mm. The disks had to be thin enough to maintain a radial overlap between middle and outer modules to maintain hermiticity of coverage. The maximum thickness to achieve this was 8.7 mm, which is rather thin for such a large structure. This gives the disks a low out-of-plane stiffness, so that small asymmetries in the manufacture (e.g. thermal gradients during curing, or non-flatness of the close-outs) can potentially cause large deformations in disk flatness. The tight tolerance of 0.5 mm was necessary to be certain that there would always be adequate clearances between modules and services. PCI made major efforts and succeeded in achieving a typical flatness over the whole disc of 0.3 mm. To help reference the disks in angle, a yellow aramid fibre was embedded in the surface.

The disks were delivered to NIKHEF where they were made ready for module services [14]. Firstly two reference alignment holes were added at the inner radii. CFRP inserts were embedded at 12 points around the outer circumference to allow the disks to be held in the support cylinder – these were tested to 100 N. Next apertures and through holes for inserts were machined using a large reference plate. The apertures, which allow services to cross from one side to the other, were subsequently sealed with molded CFRP closeouts.

Various inserts were added, in particular, pads to provide the attachments for the cooling circuits. Jigs were used to place the pads with a tolerance of 300 m. The pads were made of Torlon® which is easily machined and very stable against creep and were glued to the abraded disk surface using epoxy. It is important that the surfaces of the pads are flat and planar, so as to ensure the modules are parallel to the disk surface, to ensure sufficient separation between neighbouring modules (the minimum separation between adjacent modules in height is 1 mm – wirebond to wirebond) and to avoid distorting or stressing the modules. This was achieved by clamping the disk to a stiff, flat metal plate and machining the whole disk in one go to achieve the tolerances set out in Tab. 4.

| Dimension | Value | Tolerance |
| --- | --- | --- |
| Width between insert outer surfaces | 15 mm | ±0.1 mm |
| Flatness of insert surfaces | 0 m | ±50 m |
| Slope of insert surfaces relative to disk plane | 0 mrad | ±1 mrad |

Tab. 4. Tolerances for the machined disks.

Fig. 2. Completed machined disk being measured on a CMM.

### Quality Control

The bare disks were checked at NIKHEF for stiffness, resonance frequency, weight, and geometrical tolerances. Geometrical tolerances were measured with a 3D CMM (Coordinate Measuring Machine). The most demanding tolerance was the flatness, which was also difficult to measure: a disk is not very stiff, so tends to deflect under its own weight and the pressure of the measurement probe. Therefore the disks were held vertically during measurement – see Fig. 2. They were mounted kinematically by three points and then an additional three support points were added. Tab. 5 summarises the measured properties of the disks.

| Property | Mean | R.m.s. |
| --- | --- | --- |
| Mass (g) | 1210 | 30 |
| Natural frequency (Hz) | 42 | 2 |
| Static stiffness (units) | 32 | 1 |
| Flatness (front and rear) (mm) | 350 | 85 |
| Thickness (mm) | 8.82 | 0.04 |
| Inner radius (cf Tab3) (mm) | 266.97 | 0.07 |
| Outer radius (mm) | 567.09 | 0.03 |
| Inner circularity | 0.10 | 0.05 |
| Outer circularity | 0.13 | 0.08 |
| Concentricity | 0.08 | 0.06 |

Tab. 5. Properties of the machined disks. WERNEKE

The positions of the mounting pads were measured for all disks. These measurements were repeated at RAL [15] for the first two disks to ensure there had been no deformations during transportation. All the pads measured were well within tolerance (( 300 m). An example of the displacements of the pads is shown in Fig. 3. For the example of Disk 9C, after allowing for global rotation of all the pad positions with respect to the dowel holes, the rotation of the main (secondary) pads had an r.m.s. of 49 (44) m and maximum values of 100 (150) m.

Fig. 3. Displacements of pads from their nominal position for main and secondary pads (outer modules) for Disk 9C. The positions are in mm, and the displacements are magnified by 1000.

### Properties of the Disks

A number of prototype disks were made to test the manufacturing techniques and confirm the FEA models [16]. Initial calculations of the frequency were found to be 20% higher than the measured values. Adapting the model then gave a good description of the measured stiffness. The FEA model of the final disk design included the apertures, closeouts, inserts and services and modules. The first natural frequency is a “conical” mode at 22 Hz, shown in Fig. 4. In-plane displacements are mostly due to the CTE and CME effects, leading to expected movements of 230 m/m. When going from room temperature and a relative humidity of 50% to the cold and dry environment for operation, out-of-plane distortions not exceeding 40 m [16]are expected to arise from the force of the cooling pipes (see Section 2.2.1), since the circuits are assembled at room temperature and yet operate around 20oC. Variations in the operating conditions of 2oC will result in displacements of only a few microns.

Fig. 4. First vibrational mode of a disk.

## Services

The modules are held on the disks by means of the blocks which also provide cooling (Section 2.2.1. Each module has electrical power supplied by a “wiggly” power tape (Section 2.2.2.1); it receives timing, trigger and control (TTC) information from one optical fibre (TX) and is read out by 2 optical fibres (RX) – 2 fibres increase the band-width and provide redundancy.

Each disk is instrumented with its own services [17] which terminate at the outer radius of the disk at a set of patch-panels denoted generically as PPF0. This allows disks to be tested before and after the modules are mounted – after modules are mounted, repairs to the services become very difficult. The services for a disk with all module Rings are shown in Fig. 5.

Fig. 5. Services for Disk 6 front (left) and rear (right).

There are variations in the services required for each disk depending on which rings of modules it carries. The stereo rotations of the modules (described in Section 1.2) also cause differences between even-numbered and odd-numbered disks. Fortunately, this only affects the cooling circuits which are rigid, the other services are flexible and can accommodate small movements in the location of the module hybrids O(1) mm.

### Cooling Circuits

#### Design

The circuits are required to keep the silicon of the SCT modules at 7oC. They are manufactured from copper-nickel (Cu-Ni) 70:30 tubing with 70 m wall thickness and 3.74 mm outer diameter. Cu-Ni was chosen since it is fairly resilient to corrosion and easily joined by standard soldering techniques.

There is a separate circuit for each quadrant of each ring, so there are either 13 (outer ring) or 10 (middle & inner rings) modules per circuit. The circuits are manifolded together on the exhaust side at PPF0, resulting in quadrant modularity on each disk. Because the choice was made to have rigidly fixed cooling circuits, stress-relief was incorporated by making the circuits “wiggly”, as illustrated in Fig. 7. Cooling is supplied to the module in the region of the hybrid by a section of the circuit which is approximately radial. In the case of the outer and middle modules, cooling is also supplied at the far end by a circumferential section of the circuit. For the inner modules, no far end cooling is provided due to the modules having approximately half the area of silicon and no mid-point break, hence additional cooling was deemed unnecessary.

Fig. 6. Cooling circuit for middle modules: design (left) and realisation on a disk (right).

Fig. 7. Cooling blocks: main (left) and secondary (right).

Cooling is supplied to the modules via cooling blocks: “main” cooling blocks in the vicinity of the hybrids, and “secondary” cooling blocks at the far end of the modules. These blocks are attached to the cooling circuit by soft solder and screwed down to the CFRP disk. The solder provides a connection which is not too rigid, accommodating the different CTE’s of the blocks and pipes. In turn, the modules are attached firmly to the blocks. The blocks are made from carbon-carbon – a form of graphite with high thermal conductivity in one plane (typically ~100 W/m(K, max ~300 W/m(K) and poorer conductivity out of the plane (~50 W/m(K, max 150 W/m(K). The blocks have an aluminium threaded pin over which the module is placed and secured by a Belleville washer and small nut. The module hybrids generate more heat than the silicon detectors and the module design has attempted to minimise the thermal isolation of the two sections of the module. This isolation is ensured in the cooling block by a PEEK split separating two sections of carbon-carbon (visible in Fig. 7): the larger section of the block being available to cool the hybrid, while the smaller section is in contact with the “spine” supporting the silicon [3]. The plane of high thermal conductivity of the carbon-carbon is chosen to be parallel to the split. Thermal contact is ensured by pressure from the module nut and a controlled layer of thermal grease 20 m thick. To ensure that the modules did not violate their envelope, potentially risking mechanical contact or electrical discharges with neighbours, and to avoid distorting the modules, the blocks were required to have a height variations no more than 20 m and the height variation between the blocks at either end of a module should be no more than 100 m.

The capillaries carrying the coolant to the disks (each associated with a single circuit) terminate at the cooling PPF0. However, the exhausts from all the circuits in one quadrant of a disk merge at PPF0, implying that a significant leak in a single circuit could cause the cooling for up to 33 modules to be lost. Both the inlets and exhausts are connected by aluminium seals. These are small rings with a metal jacket containing a spring. The seals are intended to be compressed in such a way that the metal jacket conforms to the surfaces of the housing, while the spring keeps the jacket pressed against the housing despite any movement due to thermal effects.

Initial Finite Element Analysis (FEA) calculations [18] using CFX [19] indicated that in the gas between the disks, convection would give a temperature difference between the top and bottom of up to 14oC. The simulations were broadly confirmed by a mock-up [20] which found significant heat-flows into the outer and middle module rings at the top of the End-cap and into the inner modules just below the ITE. This convective heat load on the front face of the modules, plus a load on the back face from the power tapes, plus a factor to account for uncertainties, amounted to 0.8 W for middle and outer modules and 0.4 W for inner modules. The modules have been designed to tolerate these loads from their environment without over heating.

#### Prototyping

There was some consideration given to a design where cooling pipes would run circumferentially around the disks. To cope with contraction of the circuits, required sliding joints and the concern was that either the grease joint would fail or the modules would be pulled out of position. Although this design had less material, it was abandoned in favour of the “wiggly” circuit design described in 2.2.1.1, since the latter naturally incorporated stress relief.

The original intention had been to manufacture aluminium cooling circuits with aluminium cooling blocks. This worked well using tubing of 200 m wall thickness and the cooling blocks were easy to manufacture using CNC machining. The problem was how to connect the blocks to the pipes with a low thermal resistance. Soldering on selectively Cu-plated areas worked well, but produced an interface between two metals of very different electrochemical potential which was shown to be susceptible to corrosion in the presence of moisture – this was especially true at the edge of the sputtering region, where pin-holes formed. For this reason, this solution was dropped and replaced with Cu-Ni. Because the radiation length of Cu-Ni is much higher, a reduced wall thickness of 70 m was chosen to minimise material effects. Unfortunately the Cu-Ni proved significantly harder to bend into “wiggles”. The move to carbon-carbon cooling blocks benefited from a factor of three increase in radiation length, but due to the difficulty of machining complicated shapes, the actual improvement in material was more like a factor of two. This partially compensated for the increased material coming from the Cu-Ni pipes

Several prototype cooling blocks were tested with C3F8 evaporative coolant operating around 18oC. It was found that the dominant thermal impedance was between the pipe wall and the coolant itself. This was determined by measuring the heat transfer coefficient (HTC) for some simplified blocks. The HTC is a function of the coolant flow rate, vapour fraction and power density. It was found that in the expected regime, with a flow rate around 2 g/s and vapour fractions in the range 10% to 85%, the HTC is mainly a function of power density, P (W/cm2), and can be conservatively represented by HTC = 330×P+1800 (W/K/m2). The result for the final block design with a 1 mm PEEK split was that at maximum module power, the detector and hybrid halves of the block ran at 8 and 13oC respectively above the coolant temperature. Finally, an irradiated inner module was tested on a prototype of the final block design and was stable against thermal runaway up to a coolant temperature of 5oC.

The original design for the cooling connections at PPF0 involved aluminium seals. These were subjected to a qualification procedure comparable to that described in Section 2.2.1.3 and were accepted on the basis of 10 of them passing. To avoid possible corrosion problems associated with moisture, copper seals of a comparable design were considered. This solution was abandoned in the light of difficulties in compressing the stiffer seals so as to cause the rims of the housings to come together forming a stable connection. Nevertheless, the requirements of low-mass connections and the limited space available makes it difficult to have housings capable of supplying substantial compression forces.

#### Manufacture

Bending the Cu-Ni tube to form wiggles of the required bend-radius (4×diameter) proved to be difficult because of the tendency of the tube to either crease on the inner side or rip on the outer side. Test were made using fillers consisting of ice, “sand” (very small glass beads) and low-melting-point metals (Cerabend®). The first two were not successful; the Cerabend® worked well but left residues inside the pipe, giving concern that the material might flake off and subsequently cause blocks in the cooling system. The solution adopted was to bend the tubing in air using carefully designed tooling with suitable torques. After much testing, this resulted in a cross-section reduction of only 20%. Due to small differences associated with the stereo module geometry, some portions of the circuit were different for the different orientations. The completed sections of pipes corresponding to the main cooling blocks were checked in a go-no-go jig with tolerances around ±100 m – this tolerance ensures that the stresses on the disk are not too great. Pipes which did not drop naturally into the jig were adjusted if possible to ensure conformance.

The carbon-carbon blocks were difficult to machine – the material has an appearance and texture comparable to a balsa-wood. This resulted in a simplification in the design. Since the blocks are critical to the location of the silicon modules, a 10% sample was measured and found to be well within specification. To prevent the absorption of the thermal grease, the blocks were coated with 1 m layer of gold on top of 12 m of copper. The module location pin was inserted through a hole, located by shoulders on the base of the pin and fixed in place by solder. The blocks were located relative to the pipe by an accurate jig and soldered in place. Different sections of the pipe were connected by soldering them together with enlarged sleeves to create complete circuits.

Once the circuits were assembled, they were then cleaned and tested. The first step was to clean the internal surface of the pipe by flushing and soaking the system overnight with a commercial cleaning fluidl and a dedicated cleaning rig with removable filters and a fume extraction system. Any leaks which developed, due to the removal of flux by the liquid, meant that the system had to be drained and dried with nitrogen before any repairs could be undertaken. After successful cleaning (established by visual examination of the removable filter), the pipes were flushed with nitrogen to dry the surfaces.

The system was then pressure tested to 25 bar with helium. With the disk inside a sealed enclosure, a helium leak-detector was used to sample the volume and check for leaks. The pipe was then vented and connected to a vacuum pumping system to ensure that a pre-defined vacuum pressure could be achieved. Helium was then introduced into the sealed enclosure and the helium leak-rate checked.

### Other Services

#### Power Tapes

Power is supplied to the modules and opto-packages via “wiggly” power tapes [21]. These tapes also contain voltage sensing lines, the temperature reading from the module and control lines. In the original design, aluminium tracks were sandwiched between layers of polyimide. This resulted in wide tapes on which the aluminium tracks were prone to cracking and difficult to solder to. Further, because of their width (about 1 cm), complicated routings were required in order to lay the tapes on the disk surface without overlap. For these reasons, the design was changed to copper tracks with a twisted pair for the main current-carrying conductor.

The low-current power lines, temperature monitoring and control lines are on double-sided Cu-polyimide tapes. The copper is 18 m thick and the polyimide is 25 m. The lines are 150 m wide with a 150 m gap between traces, except for the high voltage (HV) line which has a separation of 800 m to the nearest line in order to minimise leakage currents. In addition, a polyimide cover-layer was used to provide isolation. In the region near the connectors where there was no cover-layer, the separation between the HV line and the neighbour lines was increased to 2.5 mm. The first tapes were produced with a 50 m thick photo-imageable cover-layer. However, the resulting tapes were found to be rather fragile; so for the rest of the production, a conventional polyimide cover-layer was used. The low-voltage (LV) digital and analogue power for the module (higher current) is carried by twisted pairs made of 0.55 mm diameter copper-clad aluminium (CCA) with an insulating lacquer coating, with 2 turns per inch. The wire composition by volume is 90% aluminium and 10% copper. The CCA twisted pairs were attached to the Cu-polyimide tapes with sticky polyimide tape. As the CCA is much more rigid than the Cu-polyimide, this tended to cause breaks in the narrow copper traces when the tapes were bent into the required 3D shape. In retrospect, a more robust design would have kept the CCA twisted pairs and Cu-polyimide tape mechanically separated.

To reduce the numbers of flavours of tapes, power for up to three modules is incorporated in a single tape – the three modules sharing a common tape will have similar azimuthal position but not necessarily be in the same rings. The ends were rigidised for stress-relief and terminated with connectors for connection to the module hybrids at one end and the PPF0 at the other. The CCA twisted pairs were soldered to pads on the tape near the connectors. Due to the mismatch in the number of modules in the different rings causing the modules not to line up in azimuth and the absence of inner modules on four disks, the only replication which occurs is by quadrant and 21 different “flavours” of tapes are required. A typical tape is shown in Fig. 8.

Fig. 8. A typical “wiggly” power tape to power two modules. The module connectors are at left and middle; the PPF0 PCB is at right. The LV twisted pairs can be seen above the polyimide flex circuit.

#### OptoHarnesses

Data from the detector is transferred to the off-detector electronics by optical fibres. Timing, trigger and control (TTC) data are also transferred from the off-detector electronics to the detector by optical fibres. Two data and one TTC fibre serve one detector module. The data (TTC) fibres from between 4 and 6 modules are spliced into 12-way ribbon fibres to form a fibre harness. More information on the fibre harnesses is available in [22]. One critical issue for the harnesses associated with the engineering was that the fibres have to be light-tight in order to avoid generating noise in the silicon detectors. This meant that the individual fibres were in 0.9 mm OD black furcation tubing and the ribbons were wrapped with aluminium foil. Unfortunately the black furcation tubing was difficult to see next to the carbon fibre. Because the fibre routing was complicated, it had to be performed by hand. Very thin furcation tubing was required because of the tight clearances, consequently it provided little protection for the delicate fibres and there were several fibres damaged during the assembly which required the harnesses to be removed from the disk.

#### FSI (Frequency scanned interferometry)

The ATLAS FSI alignment system is documented elsewhere [7]. Each SCT End-cap is equipped with 165 grid line interferometers (GLI’s) in the disk planes and connecting adjacent disks. Altogether, they make an over-constrained grid. Details of the End-cap layout can be found in [9]. The length of the GLI’s can be measured to better than 1 m by virtue of interferometry with variable light wavelength. Variations in the measured GLI lengths indicate distortions of the disks or relative movements of the disks. Only relative motion (potentially caused by thermal effects or the relaxation of the support structures) can be determined, since the absolute positions of end-points of the light paths are not known acurately. The FSI system provides information on correlated displacements of modules and hence is very important for determining large-scale deformations of the detector – this is highly complementary to the information provided by the offline alignment using reconstructed charged tracks.

Each GLI is formed by a pair of a “quill” and a retro-reflector. Quills are assemblies of a delivery and a return single-mode opto-fibres attached to a glass beam-splitter. Each quill emits a cone of infra-red light (opening angle approximately 2.5o) directed towards the retro-reflector. The reflectors are made from small aluminium cylinders, 2 mm in diameter, into whose surface was punched an accurate cube corner; the cylinder was subsequently gold-plated. The reflected light is received by the same quill into its return fibre, detected by an APD at the other end and subsequently subjected to interferometric analysis with respect to a stable reference length. For the method to be accurate, it is important to monitor the temperature of the ambient gas in the vicinity of the light-path and to ensure a stable gas composition.

Grid nodes which contain end-points of several GLI’s are made into so-called “jewels” which hold individual quills or retro-reflectors. The grid is complicated and the location of the nodes varies from disk to disk to adapt to changing disk spacing. Typically there are three jewels at the outer disk radius and three or six ones on the inner radius. One side of the disk is equipped with jewels holding mostly quills while the other side contains jewels with retro-reflectors only. GLI’s are formed between the outer points, from the outer to the inner points and between the outer points and the inner points of the neighbouring disk. The jewels are predominately made from glass-filled Torlon® which is a plastic stable to moisture and temperature variations. To have lines of sight above the rest of the services, the jewels are supported on a pair of thin quartz rods and mounted on a PEEK base which is fixed to the disk. The jewels need to be mounted with a spatial precision of better than 1 mm and angular precision of better than 1o. Example jewel assemblies are shown in Fig. 9.

Fig. 9. Typical FSI jewel (left) and reflector (right). Note the thermistor mounted to the right of the jewel.

The optical ribbons from individual jewels run to the dedicated splice boxes attached to the EM calorimeter cryostat with no break at PPF0, in order to minimise light loss and internal reflections. There, they are spliced into multi-ribbon cables which route the light to the readout crates.

#### DCS

Sensors for the Detector Control System (DCS) were placed all over the disks. Up to 30 thermistors were placed on each disks, and in particular on the FSI Jewels. These consist of flat 1 k thermistors encased in polyimide and read out with twisted pairs. Each disk was instrumented with a single humidity sensor consisting of a three-wire package in a carbon-fibre housing.

#### Patch Panels (PPF0)

There are patch panels for most of the services at the outer radius of each disk on the rear side.

There are four cooling patch panels per disk consisting of the inlet and exhaust connections, described in Section 2.2.1.2, along with the associated support bracket.

There are 16 electrical patch panels per disk. These consist of the rigidised ends of the “wiggly” power tapes held in brackets. Each patch panel serves up to 9 modules via 3 3-way tapes (note: not all positions are used). There are 8 optical patch panels per wheel and 4 for DCS.

The patch panels for Disk 9 are on the front side, since the disk has been rotated back-to-front (see Section 1.2). This requires some modified circuitry on the ends of the “wiggly” power tapes to cope with the swap to the order of the power lines.

#### Miscellany

To ensure that the wheels and associated services are grounded, aluminium-polyimide foils are placed on the disks. The foil is plated to allow good solder connections to be made: polyimide (25 m), glue (25 m), Al (50 m), Ni (12 m), Au (2 m). There are two foils; one on the front and one on the back of the wheels which cover approximately 6% and 19% of the surface area respectively – see Fig. 10. The foils are connected to the ground pads on the CFRP disk and to the cooling circuits by soldered tabs. In turn, the cooling circuits are connected to the ATLAS ground via connections to the ground sheet on the support cylinder (see Section 4.2).

Fig. 10. Front ground foil for a disk.

### Services Assembly and Testing

The assembly of all the services to each CFRP disk took 3-4 months, including testing. Services were added one layer at a time: grounding foils, wiggly power tapes and optoharnesses. These were tested before they were trapped by the rest of the services: cooling circuits, DCS and FSI jewels. Extensive testing was undertaken of the power tapes, the optoharnesses [22] and the cooling circuits. Any significant damage of the tapes or harnesses required that the cooling circuits were removed to allow replacement – this was time consuming. The result was that every completed disk was fully functional.

After this, the cooling blocks, which until this point were only loosely placed, were positioned accurately. By design the screw holes in the blocks were 300 m oversized allowing the blocks to be moved and located accurately. For EC-C, the disk was paced on a digital rotary table and centralised using the two central alignment holes in the disk by viewing through an optical system. Custom made targets were placed over the pins in the blocks and the blocks were adjusted by hand to their defined positions, again by viewing under the same optical system. Once located, the block retaining screws were tightened to a pre-defined torque. At the same time, the base-pads for the FSI jewels and reflectors were placed. For EC-A, a precision-machined plate was used. The tolerances for the pin placement to ensure that all the modules overlapped without gaps were: 37, 60 and 190 m (see Tab. 2) for the outer, middle and inner Rings respectively.

The final FSI components, which were above the silicon modules on the front of the disks, were only able to placed once the module mounting (see Section 3) was completed.

Fig. 11. Disk 6 with services, ready for modules: front (top) and rear (bottom).

# Module Mounting

## Module Mounting

Modules were mounted on to disks at Liverpool and NIKHEF using similar techniques, designed primarily to accomplish the task with minimal risks to the modules. This required the design and manufacture of tooling to allow the disk to rotate and modules to be mounted onto the cooling blocks as well as the development of procedures to dispense thermal grease (DC340), fasten down the modules and attach the services. At the start of the build, all lower modules of all ring-types would be mounted in groups of about six; the disk was tested and then module mounting resumed with the addition of the upper modules after which the disk was tested again. However, very few defective modules were found in testing, and the later disks were built without the intermediate tests.

The basic concept of the tooling is shown in Fig. 12. The disk was mounted on a rotating ring mounted in a frame which allowed the disk to be positioned at precisely the right angle so that the mounting points for all modules could be brought to exactly the same position relative to the module mounting jigs. Modules were then mounted on the module transfer plate and extracted from their frames before being located on to the cooling block pins on the disk using the module mounting jig.

Fig. 12. Tooling for module mounting.

The module mounting jigs consisted of a base and an interchangeable tower, as shown in Fig. 13. The base was mounted on precision rails running perpendicular to the disk. Left-right and up-down translation stages were used to position the tower relative to the disk. The tower supported a module grabber which allowed the module’s angle and position (in the direction of the rails supporting the base) to be adjusted. Miniature CCD cameras were used to view the relative positions of the module’s precision mounting holes with the corresponding pins on the cooling blocks to allow the operator to correctly position the module before it was slid on using the grabber.

Fig. 13. Module mounting jig.

The thermal requirements dictate that the amount of thermal grease making the cooling contact between the modules and their cooling blocks be carefully controlled. This was achieved using a precision liquid dispenser and a syringe as shown in Fig. 14. Thermal grease was applied to the main point blocks using a 10-dot pattern, whilst 6 dots were applied for the second-point blocks. The mass of grease applied was adjusted by varying the air pressure and air pulse duration on the dispenser. The mass of grease dispensed was checked before a group of five or six modules was mounted by applying grease to the sample block. The typical grease coverage over a block was checked by mounting a clear plastic plate on the sample block and applying the torque used for module mounting.

Fig. 14. Tooling for grease application to module cooling blocks.

Module mounting began with the preparation of a list of modules for each ring type selected using the performance parameters obtained during module testing at the assembly sites. The selected modules were moved to storage near the module mounting station. Typically, module mounting proceeded by ring type, block height and quadrant. For example the five lower modules in the top right quadrant (TR) of the middle ring would be mounted sequentially. Using the preliminary module lists, the five required modules were identified and laid out in mounting order. Then, the grease dispenser was set up, adjusting the parameters to get the right amount of grease, and grease was dispensed on each of the five pairs (main and far-end) of cooling blocks. The disk was positioned using the indexing holed in the rotation ring such that the blocks for the first module were at the bottom.

The first module, still held in its frame, was then mounted on the module transfer plate. The plate was slid and locked in a position immediately in front of the module mounting jig. The jig was then slid forward and locked in position. The lever to open the module grabber jaws was activated and, using the CCD cameras for feedback, the position of the grabber was adjusted using the translation and rotation stages and the grabber plunger. The grabber jaws were closed and a check was made to ensure that the module was being held properly. The module was then released from its frame, the module mounting jig was withdrawn and the module transfer plate slid back.

With the module now on the end of the grabber, the module mounting jig was advanced and positioned just in front of the disk. Again the position of the module was adjusted using the CCD image of the module mounting pins in the two cooling blocks as a reference. Once the module was correctly aligned, it was pushed onto the blocks using the plunger of the module grabber.

The module was released from the grabber and the module mounting jig was withdrawn. The module would remain in its proper position due to the slight stickiness of the thermal grease. The far-end nut was loaded into its driver. The far-end washer was located onto the pin using tweezers and the nut was screwed on until the module was just being held. This was repeated with the main point pin but with the added complication of the “grounding finger” which was slid over the pin before the washer and nut. When both nuts were on their respective pins, a torque driver was used for the final tightening.

As a final check, the distance from the top of the main-point nut to the top of the main-point pin was measured. The graph in Fig. 15 shows the values obtained for the 66 lower modules on Disk 6. Any modules with distances greater than 1.9 mm were re-checked. Typical problems were associated with the washer or grounding finger catching in the threads of the pin causing the torque threshold to be reached before the module was properly secured. Also the positions in the plane of all of the mounting pins were measured on a CMM and incorporated into the alignment database in order to provide an initial estimate of the position of each module within a disk.

Fig. 15. Distance from the top of the main point nut to the top of the main point pin.

The mounting of modules at Liverpool began on 10th September 2004 with Disk 9C and the last module on Disk 1C was mounted on 19th July 2005. The graph in Fig. 16shows the progress made.

Fig. 16. Progress in mounting modules at Liverpool (EC-C).

## Testing

After the disks were assembled, they were electrically tested [23] to check that none of the modules had been damaged during the assembly procedure. The disks were placed inside a test-box which sat inside an environment chamber where the air humidity and temperature could be controlled. The dew-point in the chamber was kept around 30°C. The modules were cooled to the nominal operating temperature of 27°C using the SCT evaporative cooling system. The modules were powered [24] using the custom made SCT power-supply system and read out optically using the SCT ROD’s (readout driver), BOC’s (back-of-crate card) and TIM (TTC interface module) [25][26].

The measured input noise for each module type is shown in Fig. 17 and the average for each of the module types is shown in Tab. 6. The numbers of defects (missing wire-bonds, bad electronic channels etc.) per module are shown in Fig. 18.

Fig. 17. The input noise for each of the module (EC-C) after module mounting..

| Module Type | Noise (ENC) |
| --- | --- |
| Outer | 1580 |
| Middle | 1532 |
| Short Middle | 907 |
| Inner | 1070 |

Tab. 6. The average input noise for each module type.

Fig. 18. The number of defective strips on each of the 988 modules for EC-C.

The total number of defects for all 988 modules from EC-C was 4205, which is an average of 4.3 defects per module. This was well below the specification of a maximum of 15 defects per module. Also of interest is the fact that no additional defects were introduced during the assembly process. This was done by comparing the number of defects on the modules before assembly to the data shown above. The results from the EC-A were very similar.

# Support Structures

## Design

The SCT End-cap support structures [27] support the disks within the Inner Detector. Each End-cap has a support cylinder, a front support panel, a rear support panel and an inner thermal enclosure (ITE) cylinder. The support cylinder locates and supports the disks, while the front and rear supports hold the cylinder on the TRT rails so that the SCT End-cap and TRT End-cap are coaxial (the TRT is in turn supported by rails fixed to the inner bore of the cryostat). The support cylinder also carries services to and from the disks. The front supports, in-fill panels (part of the front support) and rear supports along with the ITE cylinder form essential components of the thermal enclosure, discussed in Section 8.

Fig. 19. End-cap support structures, showing the main components.

The support cylinder, front supports and rear supports are composite sandwich structures using CFRP facesheets. The core of the sandwich panels is a high-performance aramid/phenolic honeycomb core. For the support cylinder, the facesheets and core were co-cured in an autoclave using an adhesive film. For the front and rear support, an epoxy film adhesive was used to bond together pre-cured facesheets and the Korex® core. Due to the large size of the panels and cylinder compared to the stock honeycomb sheets size, the honeycomb core was spliced together using an expanding syntactic film. All edges were sealed to prevent the ingress of moisture: CFRP close-outs were used for the support cylinder and aluminised polyimide films on the support panels. All these materials, especially the YSH-50A fibres and cyanate-ester, have been used in order to create structures which are stiff and low mass, with close to zero CTE (coefficient of thermal expansion) and low CME (coefficient of moisture expansion).

### Support Cylinder

Fig. 20. Support cylinder fitted with Cu-polyimide ground sheet.

Each support cylinder (see Fig. 20 and Fig. 32) is a CFRP sandwich cylinder, nominally 1943.3 mm long and 1165 mm outer diameter. The sandwich consists of two facesheets, 0.225 mm thick, and a honeycomb core of 9 mm thickness. The CFRP facesheets are arranged in three layers: in the external layers (the innermost and outermost faces of the cylinder), the direction of the fibres lies along the axis of the cylinder; in the other two layers of each facesheet, the fibres are arranged at (60º to the axis. This results in a quasi-isotropic lay-up, as used for the disks. The cylinder wall is perforated with a number of apertures; the larger rectangular apertures are for services to pass in and out from the patch panels (PPF0) on the edge of the disks (or directly from the disks in the case of the FSI optical fibre ribbons). These rectangular apertures are edge sealed with moulded CFRP “U” shaped closeouts. The ends of the cylinder are also closed-out with similar CFRP “U” sections. There are smaller, round apertures for the disk fixings (the aluminium alloy disks in Fig. 20) and through-holes which have been fitted with ULTEM® (polyetherimide) 2-part threaded inserts. The ends of the cylinders have embedded aluminium alloy inserts to support the screw fastenings which attach the front and rear supports.

### Front and Rear Supports

Fig. 21. Front support during load testing.

Fig. 22. Rear support during load testing.

The front are rear supports are both flat CFRP sandwich panels consisting of a central circular section of 1213 mm diameter and two support arms extending from this central section to a width of 2190 mm at the tips of the aluminium alloy mounts for the support mechanisms (see below). The support panels have integral inserts to strengthen locally the sandwich panel where it is bolted to the support cylinder. Another feature of both panels is the central aperture: this, along with the inner diameter of the ITE, creates space for insertion of the Pixel Detector and its services at the centre of the Inner Detector. The edges and apertures of the panels are sealed with aluminised polyimide tape. The front support is split into three separate sections: a horizontal central part with the arms and two in-fill panels (top and bottom) which complete the central circular section. The split design is essential for integration, where a mix of temporary supports and final parts are interchanged to transfer the SCT End-cap load from the tooling to the TRT End-cap rails, see Section 9.2. The front support sandwich consists of two 0.45 mm thick facesheets with six plies in the quasi-isotropic lay-up of 0º and (60º, as with the support cylinder and disks. The front support has a core of 8 mm thickness making the overall panel thickness nominally 9 mm. The rear support needs to support approximately two-thirds of the End-cap weight and consequently is thicker: the sandwich consists of two 0.9 mm thick facesheets (twelve plies, 0º and (60º) and a core of 25 mm thickness, giving a nominal panel thickness of 27 mm.

The support structure is sensitive to vibrational excitation which may occur within the experiment. This is especially significant in the axial (z) direction of the experiment where volumetric constraints within the Inner Detector only allowed for support using thin panels. The extra thickness of the rear support core significantly stiffens the panel, raising the first fundamental frequency of the support system. It was found during analysis of the system, as well as during testing, that for lower modes, the amplitude of oscillations is insignificant in relation to the stability required.

### Support Mechanisms

Fig. 23. Two of the support mechanisms which hold the End-cap to the TRT rails.

The support mechanisms are mounted on the end of the protruding arms of the front and rear support panels. The mechanism assemblies (mainly aluminium alloy) incorporate plain bearings which allow different degrees of freedom of the structure during contraction or expansion – these dimensional changes are caused by temperature or moisture changes (e.g. acclimatisation to operational temperature in the dry gas environment). The mechanisms support the full mass of the End-cap including all the internal services and thermal enclosure; they even support a proportion of the external services and services management (cable trays) up to PPF1. The End-cap mass is distributed at four points in the horizontal plane. The support constraints for each End-cap are shown in Fig. 24.

Fig. 24. Support constraints imposed by the mechanisms on the two End-caps.

### ITE Cylinder

The ITE Cylinder is a single CFRP laminate, there are fivr plies in the laminate giving a total thickness of 0.58 mm. The dimensions of the bare cylinder are nominally 2009 mm long, 507.6 mm inside diameter. As part of the Thermal Enclosure, it is fitted with thermal insulation, the gas purge inlet system and a ground sheet which defines the outer diameter of the cylinder. The front end of the cylinder is fitted with a 1.5 mm thick CFRP flange (13 plies of the T300 plain weave), while the other end is attached to rear support by the ITE brackets.

### FEA

A detailed model of the End-cap [28] using ANSYS was constructed to study the support structure. This consisted of 37,000 elements and included the disks supported by stiff (in lateral direction) springs and allowed for the services on the cylinder The overall CTE was found to be 1.4×106/oC, similar to that estimated for the disks, while the CME was estimated to be 1.0×104. The maximum facesheet stresses due to cooling to the operating temperature and the effects of gravity were estimated to be 35 MPa at the “wing-tips” of the front support, compared to a maximum allowed stress of 70 MPa. This does not allow for the additional strengthening incorporated in this region. The maximum deflections under these conditions correspond to a sag of the cylinder and disks around the position of Disks 4 and 5 of about 0.5 mm, as shown in Fig. 25. When CME effects are considered, due to the drying out of the Korex®, stresses of up to 50 MPa in the skin (compared to the allowable of 70) and 0.26 MPa in the core (compared to the allowable of 0.36) may be encountered at the end of the support cylinder. The allowables have a further factor of safety of two before failure. Temperature variations of 2oC are expected to result in movements at the position of the disks of no more than 8 m transversely and 15 m longitudinally – well within the tolerances. The fundamental mode is an axial movement at 6 Hz, while the second mode is at 24 Hz and corresponds to a transverse motion of the end of the support cylinder at the front.

Fig. 25. FEA showing the effect of gravity and CTE.

The displacements of the End-cap when subjected to vibrations were studied [29]. The power spectral density (PSD) measured at the LEP accelerator (CERN) [30] has a maximum value of 1(1011 g2/Hz at 5 Hz. Using the complete PSD yields displacements of the End-cap which are less than 1 (4) m perpendicular (parallel) to the axis. Even taking a much harder PSD measured at the Daresbury SRS where the maximum value is 1(108 g2/Hz, the maximum displacements are only 3 (40) m perpendicular (parallel) to the axis. These would not affect the statistical precision of the SCT.

## Manufacture and Testing

The support structures were manufactured by Programmed Composites Inc. (PCI). In a qualification step, a one-third length prototype of the support cylinder, including apertures, was constructed along with a number of test panels. The one-third length cylinder underwent metrology to qualify the tooling and manufacturing process. The test panels were subjected to ultrasonic examination (to check for delamination), thermal cycling and CTE/CME tests as well as bend tests and flatwise-tensile tests (FWT).

The support cylinder sandwich was co-cured in an autoclave on a cylindrical steel mandrel whose dimensions were chosen to compensate for thermal expansion during the co-curing process at 175ºC. The apertures and insert holes were machined one quadrant at a time using a template which ran along the length of the cylinder. The cylinder was indexed quadrant by quadrant in a step-and-repeat machining process. Finally the closeouts were applied along with the various threaded inserts. The laminate ITE was made in a similar way on a smaller steel mandrel. The front and rear support panel facesheets were pre-cured and assembled with the core and epoxy film adhesive on a surface table.

The completed structures underwent laser metrology as well as a “coin-tap” test to test the integrity of the sandwich structure, and in particular the adhesion of the facesheets. Furthermore, test samples were cut from the same panels from which the front and rear Supports were produced, and these samples were subjected to bend and FWT tests.

Preliminary tests by PCI led to the understanding that the core needed to be dried to avoid moisture contaminating the film adhesives. The first flat panels produced failed the FWT tests (require > 2.5 MPa), with bond failure in the film adhesive. This was attributed to moisture egress from the Ultem® inserts which were subsequently replaced with graphite. A second failure was attributed to the cyanate-ester based RS-4A film adhesive because of its sensitivity to moisture. This was subsequently replaced with FM73U with successful results.

While at the manufacturer’s premises, the complete sets of structures for each End-cap were tested to ensure that they fitted together and could support a load corresponding to the estimated weight of all of the disks and associated services plus a margin of safety. The load was applied by draping flexible lead blankets over the cylinder. The lead blankets ensured the load remained evenly distributed over the cylinder as it deformed and that it was not subjected to point loading. A proof load of more than 1.5 times working-load was applied. During the loading a laser tracker was used to measure deflections. A maximum deflection of 0.87 mm was measured, in reasonable agreement with the FEA predictions.

The most important features on the support cylinder are the holes for the fixings (see Fig. 32) which position the disks. These were required to be located to 0.25 mm. It proved difficult to measure these positions on a large structure which would only be rigid after assembly of the support panels. Ultimately this measurement was achieved by surveying the cylinder on a rotary table in a naturally relaxed state, namely standing vertically on its end, It was found that the holes were displaced by up to 2 mm. This was attributed to the difficulty of machining apertures and fixing holes in quadrants using a step-and-repeat process – the main cause of the problems being the location of the cylinder’s axis. Rectification was achieved by enlarging the holes and then precisely placing the fixings using the rotary table, a theodolite and an accurate tooling bar.

As a final step, a sheet of Cu-polyimide (18 m copper, 25 m polyimide) ground sheet was placed over the cylinder to provide a solid electrical ground (see Fig. 20). Care was taken to ensure that this had some slack so that when the SCT is cooled to its operating temperature, the sheet does not stress the support cylinder or rip.

# Cylinder Services

Fig. 26. Services on the End-cap support cylinder (se text for details).

Fig. 26 shows the service apertures for Disks 1, 2, 3 and 4 (from left to right). The Cu-polyimide ground sheet can be seen on the CFRP support cylinder. Above and below the apertures are the disk fixing springs of which there are 12 per disk. Their design allows the support cylinder diameter to change by a few microns whilst keeping the disks coaxial. Outside the disk fixings are the nitrogen exhaust circuit pipes (transparent PEEK tubes with an aluminium alloy manifold which can be seen on the left of the picture), and outside those are the low-mass power tapes (LMT’s) with their associated cooling pipes and heat transfer foils. Running along the centre between the disk fixings are the small diameter inlet capillaries for the evaporative cooling and the associated large diameter exhaust pipes. The rails for the outer thermal enclosure pass over these capillaries and pipes.

## Evaporative Cooling Interconnects

These run from the PPF0’s located on the disks to the services thermal feedthrough (STFT) at the end of the support cylinder. The inlets are Cu-Ni capillaries of inner diameter 0.68 mm for inner and middle module circuits and 0.76 mm for outer module circuits. The exception is Disk 1 with two 0.76 mm ID capillaries (outer & middle circuits) – the larger ID on the middle circuit compensates for the long capillary that is required to reach Disk 1 from its entry point at the other end of the End-cap. Both types of capillary have a 0.2 mm wall-thickness with a nominal 2.5 m length; the length was tuned to provide the same mass-flow for each capillary. The capillaries are fairly flexible and as some apertures are close to where the capillaries enter the SCT End-cap, the excess length is accommodated by coiling the capillaries on the support cylinder as can be seen in Fig. 26.

The exhaust circuits are made up of Cu-Ni tubes of two different inner diameters: 6 mm (with a 200 m wall thickness) and 8.1 mm (with a 150 m wall thickness). The circuits include a large “wiggle” (see Fig. 26) to minimize the forces transferred onto the disks via the PPF0 patch panel when the tubes contract during operation. The smaller diameter pipes are used for the wiggles; the thicker wall is a manufacturing requirement to cope with the production of the tight bends without collapse. The larger diameter pipes were used for the straight runs: the larger diameter maximises fluid throughput, minimises pressure drops and reduces material by the use of the thinned pipe walls.

## Low-mass Tapes

The low-mass tapes (LMT’s) provide the power and control signals for the modules. They connect the external cables at the PPF1 patch panels at the end of the Inner Detector to the PPF0 patch panels at the outer radius of the disks. The LMT’s were fabricated from polyimide with aluminium tracks in order to minimize the radiation length. However, after mounting the LMT’s on the cylinder, there were many cases of cracks forming in the nickel-plated regions at the end of the tapes [31]. Therefore it was decided to change to copper LMT’s. These were made from an adhesiveless polyimide material with a 36 m copper layer – these turned out to be very robust. 4.5 mm wide tracks were used for the high current (low voltage) lines and 0.5 mm wide tracks for the HV and all the low current lines.

From each azimuthal position, up to three tapes emerge from a disk; these build up as they are joined by tapes from successive disks going along the support cylinder, forming a “stack”, with as many as 27 tapes in a each stack .

Simulations associated with the thermal enclosure studies (see Section 8.4.6) indicated that without cooling, the centre of the stack of LMT’s could rise to 50oC. While this is not problematic for the tapes themselves, since they are bonded together at 90oC, it would represent a significant heat-load within the SCT. To avoid the this, a dedicated cooling system was devised.

Each set of three LMT’s running the length of the cylinder is cooled by dedicated cooling pipes which are fed from the module evaporative cooling circuit. The heat transfer from the LMT’s to the cooling pipes is aided by a set of 150 m foils clipped on along most of the pipe length. The pipes are fed from the cooling circuits of Disks 7, 8 and 9 where the missing rings of modules on each disk provide the additional capacity for cooling the LMT’s. Each set of three LMT stacks has a pipe on either side: one side is associated with a pipe from the Disk 9 cooling, while the other side is associated with Disk 7 or 8. In this way, a failure of the cooling associated with one of the Disks 7, 8 or 9 will not jeopardise the operation of all the modules in an azimuthal slice along the length of the End-cap. The 150 m foils which wrap around the tapes are held tightly to the pipes by means of Cu-Be spring clips which also serve to compress the tape stack (otherwise air-gaps between the tapes would reduce the thermal conductivity across the stack and raise the internal temperature). The edges of the foils are covered with a self-adhesive polyimide tape to avoid sharp edges which might rub on the LMT’s (because of thermal motion) causing damage over time. There are a number of foils placed longitudinally along each run of tapes, each foil is around 10 cm wide with a small gap between to allow any trapped moisture to escape; it is essential that no moisture forms and becomes trapped near the power track on the LMT’s, since the high voltage combined with the presence of moisture can lead to a surface breakdown of the electrical insulation and damaging short-circuits could occur to low-voltage data-lines.

Fig. 27 shows measurements across a set of three LMT stacks from a trial representing the thickest part of the stacks at the end of the support cylinder. The sections of LMT’s were powered with the maximum power density expected and the cooling was provided by room temperature water. To minimise the effect of the surroundings, the test was undertaken in an insulated box. With cooling on two sides, the temperatures across the three stacks were fairly uniform and only about 13ºC warmer than the coolant.

Fig. 27. Temperature measurements across a set of three LMT stacks.

## Remaining Services

Short ribbon fibres [22] and detector control system (DCS) services also run from the disk PPF0’s to PPF1. All the services are held in place by suitably low-mass polycarbonate or aluminium alloy clips.

The nitrogen-purge exhaust pipes are also attached to the support cylinder. There are twelve PEEK tubes with holes drilled along their length which draw in the nitrogen from the SCT End-cap volume. The gas then flows to a circumferential manifold at the front end and then back along the support cylinder and out of the End-cap.

Once all the services were attached, the cooling circuits were tested for blockages and the modules were powered, their electrical and optical circuits read out, checked and repaired as appropriate. The completed assembly is shown in Fig. 28.

Fig. 28. Services on the support cylinder before the outer thermal enclosure was added. (Note this photograph was taken at CERN at the stages described in Section 9.1, but it used for its clarity.)

# End-cap Assembly

The End-caps were assembled at The University of Liverpool (UK) and NIKHEF (Amsterdam, The Netherlands).

## Support of the End-caps

The end-caps were supported on an assembly frame made from aluminium sections. Two invar rings, the stub supports, were attached to the ends of the support cylinder using the same screw holes where the final front and rear supports would attach later. In the absence of the final supports, these rings ensured that the support cylinder remained cylindrical and provided mounting points to the assembly frame. These rings were in several sections, with cut-outs so as not to cover the complete end of the cylinder – this was essential for the integration described in Section 9. The support cylinder was mounted onto an assembly frame supported by the stub supports. Using four kinematic mounting points on the assembly frame, the cylinder was aligned so that its centre coincided with the top of the central beam. A tool to position the disks, the disk grabber, was then assembled onto the central beam and a blank disk (before services had been added) was placed in the tool which was then run along the length of the cylinder to provide the final alignment of the cylinder with respect to the central beam – see Fig. 29.

Fig. 29. A blank disk mounted in the disk grabber to align the cylinder and beam. The front stub support can be seen out the outer radius – it connects by kinematic mounts to the assembly frame at the lower corners.

## Disk Insertion

A sturdy beam was located along the axis of the support cylinder, supported from the rear support frame. The beam supported the disk grabber which allowed disks to be moved into position inside the support cylinder by use of a manual belt drive. The disk grabber consisted of three brass teeth that were machined to fit into the groove on the inner surface of the disk. The teeth were mounted on two micrometers which allowed the disk to be moved horizontally and vertically, and an additional mounting was used to rotated the disk about the centre line of the cylinder – see Fig. 30.

Fig. 30. A disk supported by the disk grabber.

To insert a disk, each disk, mounted in a support ring in the test box, was brought to the front of the support cylinder. The disk was then removed from the test box and the support ring holding the disk was then attached to the stub support on the support cylinder by sitting the support ring on pins attached to the front cylinder support. This step allowed the disk to be aligned crudely with the cylinder. The disk was then transferred to the disk grabber and the support ring removed (see Fig. 29). The disk was then manoeuvred by the micrometers until its centre was concentric with the centre of the cylinder. Next it was moved along the central beam until it was located at its correct aperture by observing some fiducial marks on the disk rim through a microscope mounted on a precisely machined bar. Then it was transferred onto a set of kinematic mounts located at 6 o’clock (weight compensator), 12 o’clock (z-movement and weight compensator) 3 o’clock (xyz-movement) and 9 o’clock (yz-movement) – see Fig. 31.

Fig. 31. One of the kinematic mounts for capturing a disk.

The disk was required to be positioned with an accuracy of better than 100 m in x and y and 500 m in z from its nominal position with respect to the cylinder. The disk was aligned in the x-y plane using two sets of optical targets which were mounted on precision-machined frames attached to the front and rear stub supports. The targets were positioned relative to dowels located in fiducial holes on the end of the cylinder, giving their position relative to the cylinder with a precision of a few tens of microns. A survey telescope was then aligned along the lines defined by the targets. This ensured that the telescope and the targets were aligned along a straight line parallel to the axis of the cylinder and the position of the line in the x-y plane was fixed to an accuracy of 50 m relative to the cylinder. The targets were located in the x-y plane to provide a line of sight through the alignment holes in the disk when the disk was in its correct position. This was achieved by moving the disk on the kinematic mounts until the holes in the disk were located on the line between the telescope and the far target. The accuracy was limited to 25 m by the markings on the target, allowing the disks to be aligned in x and y to within 50 m for Disk 9 (nearest to the telescope) and 100 m for Disk 1 relative to the line defined by the targets.

The alignment in z was carried out by placing three precision-machined tooling bars (the same bars as used to locate the fixings discussed in Section 4.2) on the cylinder, locating them with precisely placed pads on the cylinder. The holes in the bars corresponded to the apertures in the cylinder used for the fixings. These holes held a microscope, allowing it to be located relative to the cylinder with a precision in z of around 200 m. To ensure the accurate placement of a disk, it was adjusted via the kinematic mounts so that its centre line was aligned with the centre of the microscope.

After each disk was positioned inside the cylinder using the kinematic mounts, it was captured by inserting screws into the inserts in the disks – there are 12 of these per disk. The screws are held in position by springs which were designed to ensure that the stress on the disk was minimised. These springs, which are flat and made from copper-beryllium, were attached to the fixings on the cylinder – see Fig. 32.

Fig. 32. Disk fixing.

During the alignment of the disks, most of the external services on the support cylinder were absent. Since these are relatively massive, the alignment of the disks would be lost when the services would be added later due to changes in shape of the cylinder. To compensate for the absence of the services, weights were placed around the cylinder to simulate the missing mass.

A final survey of the disks showed that they were within around 100 m of the line of sight, with the most extreme case being 400 m.

## Services Assembly

The disks were inserted from the front of the End-cap, starting with Disk 9 and working back to Disk 1. As each disk was added, so the corresponding services (described in Section 5) were added to the support cylinder and connected to the PPF0 patch panels on the disk and temporary PPF1’s at the rear of the End-cap. The services were held by custom clips (as described in Section 5.3) to the cylinder and were potted into the STFT by means of Techsil® adhesive. The adhesive was silicone-based, intended to hold the services in place and yet allow them to be removed if necessary. It turned out that when the End-caps arrived at CERN, many of the services needed to be re-laid to ensure that they respected the geometrical envelopes and accurately followed the appropriate paths through the STFT in order to connect to PPF1. It was found that the Techsil® failed to dry sufficiently and so was subsequently replaced with Tempflex®.

Both the LMT’s and optical fibres were required to undergo 90o bends at the exit from PPF0 on the disk onto the cylinder and at the STFT at the end of the cylinder, where services exit the End-cap onto external cable trays. The LMT’s and optical fibres had well defined minimum bend radii and these had to be respected at both points. For the LMT’s, the geometry of the exit at PPF0 led to a natural bend that conformed to the minimum bend-radius but, at the STFT, a jig with correct bend-radius was required to ensure that each LMT in the stack of 9 conformed to the minimum bend-radius otherwise the envelope would be violated and it would be difficult to seal the STFT to make it gas-tight. A similar issue at the STFT arose for the fibres; but in addition, at PPF0 the bend-radius had to be controlled to ensure that light transmission down the fibre was not attenuated by micro-cracking and to minimise light leakage from the bent fibre that would result in increased leakage current in the silicon detectors. This was achieved by wrapping the fibre in aluminium foil at the bend – see Fig. 33.

Once all the LMT’s were laid, they were wrapped in the aluminium foil, as described in Section 5.2.

Fig. 33. Services at the disk aperture on the support cylinder. Note the optical fibres wrapped in aluminium foil as they exit the cylinder aperture.

## Testing during Macro-Assembly

As the End-cap cylinders were being populated with fully tested disks, further testing was undertaken to verify the continued excellent module electrical performance. At NIKHEF, the End-cap support cylinder was mounted into a test-and-transportation enclosure. This allowed the performance of disks to be checked after each had been installed into the cylinder. At Liverpool, the cylinder was periodically moved into a cold room, allowing disks to be tested in batches rather than one-at-a-time.

The testing focussed on checking the integrity of the connections at PPF0 between the disks and the power tapes, fibres and cooling pipes, and then on verifying that the additional components did not cause a deterioration in the module electrical performance. In particular, this latter part of the testing was crucial in demonstrating that whole End-cap system design was robust with respect to inter-module pick-up and external interferences.

# Transportation of the End-caps

## Requirements

The End-caps, when held in the assembly frames, weighed around one tonne and occupied volumes of the order of 3 m length, 2 m width and 2 m height. Because of the delicacy of the silicon modules, it was important that the End-caps should be transported very carefully to CERN [32].

It was required that the transportation should take place in an air-sprung, temperature-controlled, humidity-controlled lorry. The acceleration experienced by the transport box was required to be less than 3g (where g is the acceleration due to gravity) to avoid damage to the silicon modules and shaking loose connectors. The tilt was required to be less than 10o. The temperature was required to be 20 ( 3oC to avoid thermal stresses and the humidity kept at around 40% and certainly less than 80% to avoid condensation forming on the modules. These requirements are summarised in Tab. 7.

| Feature | Requirement |
| --- | --- |
| Acceleration | < 3 g |
| Tilt | < 10o |
| Temperature | 20 ( 3oC |
| Humidity | < 80% RH |

Tab. 7. Requirements for End-cap transportation.

## Designs of the Transportation Boxes

At The University of Liverpool, a transportation framework was constructed around the assembly framework. To this, sturdy side-panels were attached and the whole assembly was bolted to a large steel “pallet”, designed so that the End-cap could be picked up by a fork-lift truck. This enabled the End-cap to be lifted into the waiting lorry in one operation. The completed transport box was 3.7 m (l) ( 2.2 m (w) ( 2.6 m (h), and with the pallet weighed 2.8 tonnes. The transportation box is shown in Fig. 34.

At NIKHEF, the transport box was formed by the thermally insulating panels which had been used for testing. Again a transportation frame was constructed, and slings were attached under the beams enabling the End-cap to be lifted by a crane onto a platform, from which it was then rolled into the lorry.

For both the End-caps, the assembly frames were supported from the transportation frames by wire-rope isolators. These look like large springs, but have high damping coefficients in order to reduce vibrations.

Both End-caps were instrumented with accelerometers to record acceleration in all three directions, as well as temperature and humidity. These were attached directly to the assembly frame as well as the outer box.

Fig. 34. Cutaway showing the UK End-cap (green), the assembly framework (blue), the transportation framework (red) and the pallet (pink).

## Transportation

As a prelude to the actual transportation, dummy loads were constructed to simulate the mass of the End-caps and even contained a few silicon modules. These loads were instrumented and attached to the transportation frameworks. They were loaded into a lorry using exactly the same procedures foreseen for the End-caps. Tests were undertaken on various road surfaces, at various speeds, on inclines and as a part of emergency breaking. The results from the accelerometers indicated that the procedure would be safe.

For the transportation of the End-caps, the wheels of the transportation frames were raised and the boxes were held in position by load-lock bars fixed to the sides of the lorries. For the NIKHEF End-cap, additional ballast was added to the lorry to ensure the load carried was at the mid-point of its specified range. Just before departure, the accelerometers were checked. The transportation proceeded to Geneva along main roads, avoiding the Jura mountains. In the case of the UK End-cap, the transportation was handled from Liverpool to CERN by Danzas-DHL. The End-cap was required to travel by the Channel Tunnel, where the pitch of the ramps to the train is of the order of 6o.

The journeys were carried out at maximum speeds of 80 km/h, taking around two days. On arrival at CERN, the accelerometers were checked, the End-caps unloaded using the reversed procedures and then they were subjected to extensive visual inspection. During the journeys, no damage was sustained. Once the lorry was sealed up, the UK End-cap temperature remained between 17oC and 19oC, while the humidity did not exceed 60% RH. The largest acceleration experienced by the inner accelerometers (see Fig. 35) was 1.2 g, while the outer one experienced 1.8 g.

Fig. 35. Accelerations in three directions experienced by UK End-cap (EC-C) during Transportation.

# Thermal Enclosures

## Requirements

The End-cap thermal enclosures [33] must be consistent with the requirements set out in Section 1.3. The thermal enclosure must:

- Contain the SCT End-cap environmental gas and prevent significant flow of different types of gas in and out. The leak rate for each End-cap should be less than 9×104 l/h in order to avoid contaminating the TRT. Ideally, it should be much less than this. In this role, the thermal enclosure will also provide a moisture barrier.

- Provide a thermal barrier such that the heat flow between the SCT and the surrounds is a small fraction of the heat generated within the SCT so that the cooling of the modules is not compromised and there is no exchange of heat with the Pixel detector.

- Ensure that the SCT environmental gas is at 7(4(C while the external temperature is 22.5(2.5(C.

- Prevent the formation of ice or condensation on the external surfaces of the SCT in the case of moist gases around the apparatus. This requires that the external surfaces should be maintained above the ambient dew-point of 12ºC. Moist air will be present during access or maintenance or as a fault condition during operation.

- Provide a Faraday Shield.

- Not affect the stability of the internal supports and hence the modules.

The original concept for the thermal enclosures was based on active cooling, whereby the inner surfaces would be cooled and the outer surfaces heated to maintain a thermal gradient over a short distance. This was abandoned for reasons of cost and engineering complexity and it was found that passive cooling through insulation would suffice, albeit complemented by heaters to maintain the external temperature above the dew-point.

## Design Overview

The End-cap thermal enclosure design [33] consists of

- Outer thermal enclosure (OTE) – a cylinder surrounding the support cylinder and its associated services.

- Front support – since most of the front of the End-cap faces the SCT Barrel, which will be cold, no significant heat flow is expected and hence no significant insulation beyond that provided by the sandwich construction is needed.

- Rear thermal pad – to complement the insulation of the rear support, an insulated pad was constructed.

- Inner thermal enclosure (ITE) – since the inner bore of the SCT End-cap faces the warmer Pixel services inside the pixel support tube (PST), the ITE cylinder (see Section 4.1.4) was insulated.

To cope with the presence of moist air, most of the external surface of the End-cap is covered with heater pads (see Section 8.4.4) and heat-spreaders. The volume between the ITE cylinder and the PST will be flushed with dry gas and hence does not need heaters.

The layout of one End-cap thermal enclosure assembly is shown in Fig. 36. The thermal insulation is provided by Airex® foam. This is a closed-cell polyetherimide (PEI) foam which has low thermal conductivity (0.036 W/mK), low moisture absorption (a few grammes per m2 when in high humidity) and low density (60 kg/m3). To seal the foam against gas and moisture exchange and provide structural strength, composites with films of either aluminised polyimide (<1 m layer of aluminium) or Cu-polyimide (18 m copper, 25 m polyimide) were applied using Araldite® 2011. The aluminised polyimide reduces the radiative heat transfer as a result of its low emissivity and the Cu-polyimide provides excellent electrical shielding.

Fig. 36. End-cap thermal enclosure assembly, showing the main components.

Dry nitrogen gas is circulated at a rate of 850 l/h` at 15oC. To ensure no ingress of carbon dioxide, an overpressure is maintained which will be around 1 mbar, but with a limit of 4 mbar, ensured by a remotely located liquid bubbler overpressure device.

## Prototyping

### Glue Applications

The glue used was the two-component Araldite® 2011. It is important that there is good adhesion between the polyimide films and the Airex®. In applying the glue to the polyimide, it was difficult to obtain a uniform layer of sufficient thickness. Instead, better adhesion was obtained by “dabbing” the Airex® with the glue rather than painting it. Because of the rough surface of the foam resulting from cutting the cells, the Airex had the potential to absorb large quantities of glue. It was found that the peel strength did not vary greatly with glue density, provided a minimum of around 100 g/m2 was applied – this corresponds to an average thickness of 100 m. To reduce the viscosity of the glue, it was found easier to keep the components around 30oC and to work with a room temperature of 25oC. The elevated temperatures increased the cure rate, and this could be reduced by placing the glue in a wide flat tray, since the curing process is exothermic.

### Small Cylinders

Several small 30 cm diameter prototypes were made – being smaller made the handling of the glue easier but corresponded to a much smaller bend radius and more problems with creasing. Several prototypes with the correct diameter but shorter length were also produced, and a 0.5 m length prototype was assembled in order to evaluate all the assembly steps. The best results for adhesion between the polyimide films and the Airex® foam was obtained using vacuum-bagging. This worked well for the application of the foam to a layer of polyimide held on a stiff mandrel. However, in applying an outer polyimide layer separately, creases were introduced. Hence it was found to be best to glue the outer layer of Cu-polyimide to the Airex® and then when dry, to apply the composite sheet to the inner layer of aluminised polyimide already on the mandrel.

## Design and Manufacture

### OTE

Each OTE is a cylinder of 8 mm thick Airex® with an inner skin of aluminised polyimide and an outer skin of Cu-polyimide. There is an integrated flange in the region of the feedthrough constructed in the same way, albeit with 5 mm foam, and a 3 mm wide CFRP ring at the outermost radius where precision holes are located. A second ring made by gluing two 180º CFRP pieces is added on the inside of the cylinder.

Both OTE’s were constructed in the Instituto de Fisica Corpuscular (IFIC), Valencia. Several sheets of Airex® were glued edge-ways to form one large sheet, to which Cu-polyimide was glued using a vacuum-bagging technique. Aluminised polyimide was wrapped on a mandrel formed from a 3 mm steel sheet held by accurate circular ribs. The foam was then coated with glue and wrapped on the mandrel. The foam was 0.6% longer than the design circumference of the OTE, allowing it to be compressed using vacuum-bagging. When the glue dried, this resulted in a very stiff structure. The circular flange was made on a surface table and glued to the cylinder. The inner sheets of aluminised polyimide were connected to each other by Cu-polyimide tabs using a silver-loaded glue and jagged chromium strips glued to the cylinder. The outer Cu-polyimide sheets were connected by applying a thin layer of solder covered by a thin strip of copper foil to form a smooth, flat solder-joint of low resistance (discussed further in Section 11.1). One completed OTE is shown in Fig. 37.

Fig. 37. Outer thermal enclosure in its transport frame.

Each OTE is held on the support cylinder by eight composite rails made of CFRP face-skins with Airex® cores. These are very stiff but light. All sharp edges were removed, allowing the OTE to be slid easily onto the End-cap.

### Rear Thermal Pad

The rear thermal pad was a simple disk of 12 mm thick Airex® foam with skins of aluminised polyimide. Its design is such as to result in a radial gap of about 1 mm between the inner radius of the support cylinder and the outer radius of the ITE. The pad was cut from a flat sheet with a water jet and the edges were sealed with strips of aluminised polyimide.

### ITE

Each ITE consists of a CFRP cylinder (see Section 4.1.4) covered with 5 mm thick of Airex® foam. The foam is covered in Cu-polyimide to complete the Faraday shield surrounding the End-cap. The foam includes eight longitudinal channels which supply the dry nitrogen environmental gas. The gas is supplied by a pipe which is external to the End-cap and attached to the ITE at a filter which is intended to prevent the small apertures from being blocked.

Both ITE’s were completed at CERN. The foam was machined with a router to form the gas channels which were lined with aluminised polyimide. Then the foam was covered with Cu-polyimide. Holes were made in the Cu-polyimide over the channels corresponding to the gaps between the disks and small copper disks with precision 300 m apertures were soldered in place. The aperture size was chosen to ensure a sufficient flow of dry nitrogen so as to cope with the initial out-gassing of the support structures, avoiding condensation [34]. The complete sheet was then glued onto the CRFP cylinder and compressed with a vacuum-bagging technique. To avoid crushing the thin cylinder, it was supported on the mandrel used for its manufacture. Because the mandrel was slightly smaller in diameter than the cylinder, when the sheet was applied to the first cylinder, a small bump O(1) mm was produced along its length. This was avoided for the second cylinder by wrapping the mandrel with thin sheets of paper. Gas was flowed through the channels before the filter was added to ensure there were no blockages in the apertures. One completed ITE is shown in Fig. 38.

Fig. 38. Inner thermal enclosure being inserted into one End-cap.

### Heater Pads

To maintain the external temperature of the SCT End-caps, they are covered in thin heater pads. These are formed from copper tracks sandwiched between two sheets of polyimide. The copper tracks wind back and forth filling the surface area. The tracks are etched from 8 m foil with track widths between 0.2 and 2 mm and separations between parallel lines of the order of a few millimetres. There are two tracks in parallel to provide some redundancy against failures. Each circuit is designed to produce at least 150 W/m2 or 300 W/m2 depending on where it is located. The temperature of the pads is monitored by embedded thermistors which feed-back to the power supplies. The pad temperature is regulated by switching the power with a frequency of the order of 1 Hz and a rise/fall time of 1 ms. Because of the complicated shapes of components of the End-caps, in particular around the feedthroughs, twelve different types of heater pads are needed, giving a total of 40 heaters for each End-cap, each capable of producing a maximum of the order 100 W power. An example showing the design of one type of heater pad is shown in Fig. 39.

Fig. 39. Heater pad for one of the front support in-fill panels (see Section 4.1.2) and an enlargement.

### Membranes

Membranes at the front and rear of the support cylinder (just inside the front and rear supports) serve to complete the Faraday shield and provide a gas seal.

The rear membrane consists of a large sheet of Cu-polyimide extending from the ITE to the STFT, where it wraps over the flange on the OTE. Where the membranes have to bend round corners, tabs are formed by slitting the sheet at intervals of a few cm. To prevent tears, the ends of the slits are terminated with small holes. Contact between the tabs and the other Cu-polyimide surfaces is made by solder bonds. The holes to allow the rear support to be bolted to the support cylinder are sealed with Tempflex®. These holes were created using a circular punch in association with a large template.

It is expected that when the SCT cools from room temperature to its operating temperature, the membranes will contract by around 300 m. To avoid the substantial stresses which will be created in the membranes (around 1000 N per metre of circumference), “V” creases were placed in the tabs to accommodate the contractions.

At the front, for assembly reasons, there are two membranes: a gas membrane made of plain polyimide and a grounding-and-shielding membrane made of Cu-polyimide (see Fig. 40).

Fig. 40. Front grounding-and-shielding membrane ready to be soldered to the OTE. The “V” creases in the tabs can be seen at the outer radii.

### FEA Studies

Early FEA studies of the mechanical properties of the OTE [35] showed that the effect of a 4 mbar overpressure would produce an increase on the radius of less than 10 m, while the effects of cooling from room temperature to the operating temperature would result in a contraction of a few hundreds of microns.

Extensive studies [36] of the design concepts were undertaken using analytic calculations and FEA (using ANSYS). It was found that the heat exchange with the nitrogen purge gas will be negligible however the gas is responsible for increasing heat flow into the End-cap by convection at the 10% level. By using high-performance insulating materials such as Pyrogel® or Nanopore®, the heat flow could be reduced further by ~25% or ~50% respectively. However, these materials were not used because they are more difficult to handle, would need to be encapsulated and the performance of the Airex® was considered sufficient.

Fig. 41 shows a schematic summary of the heat flows associated with sources of heat (heater pads and services) and sources of cooling (LMT cooling and cooling interconnects). The net flow is an inward flux of ~200 W – this additional heat load will be absorbed by the evaporative module cooling (since this is rated at 10 kW, the additional 200 W is a small perturbation).

Fig. 41. Schematic of heat flows in the End-cap. Red arrows show the flow of heat; blue arrows show the flow of “cold”.

# Final Assembly and TRT Integration

## Final Assembly of the SCT

The two partial End-cap assemblies were shipped to CERN from their assembly sites, one from The University of Liverpool in the UK and the other from NIKHEF in the Netherlands. The assembly continued at CERN in the surface assembly building, SR1, next to the ATLAS Pit. The first additions were the shunt shields, one at each end of each support cylinder. The shunt shields are annular, composite sandwich panels with a core of 4 mm Airex® foam, to which were bonded two thin layers of Cu-polyimide foil using Araldite® 2011 epoxy adhesive. The shunt shields cover the outer modules on Disk 1 and 9, and are supported on these disks by fixing them to the module placement pins with electrically insulating nuts. The shunt shields physically protect the modules from movements of the neighbouring gas membranes, as well as shielding the modules from electronic noise. To achieve this shielding, the copper face adjacent to the modules was connected by a tab to the grounding ring on the disk, while the outer copper surface was connected to the ground sheet on the support cylinder.

The first step in preparing to integrate each SCT End-cap with the TRT [38] was to replace the invar rear stub support (see Section 6.1) by the CFRP-composite rear support panel. For this, the End-cap was supported by a temporary support ring adjusted at twelve points to rest on the support cylinder – see Fig. 42. This ring eliminated any movement of the support cylinder during the changeover as well as keeping the shape of the support cylinder. Once supported, the stub support was removed and the rear support, including part of the services thermal feedthrough (STFT), the rear grounding-and-shielding (G&S) membrane and the rear thermal pad, was assembled to the support cylinder. Next the services were sealed into the STFT using Tempflex® silicone sealant and the front section of the radial cable tray (RCT) was assembled onto the rear support. The RCT is a segmented aluminium annular plate extending between the STFT and the cryostat, with lidded channels to support and contain the services. The RCT is used in conjunction with the cryostat cable trays (again with lidded channels) to contain and protect the services up to PPF1.

Fig. 42. Removal of the rear stub support, during which the End-cap is supported by a temporary support ring.

For integration with the TRT End-cap, the SCT End-cap and its services (on intermediate supports) had to be transferred from the original assembly support frame to a higher position on a cantilever beam. First the SCT End-cap and support frame were placed on a trolley using a jacking system, with fine adjustments of the trolley and beam undertaken for accurate alignment. The trolley was slowly manoeuvred along precision guide-rails so that the End-cap passed over the beam. Once in place, a final alignment was undertaken before transferring the load from the assembly frame to the beam.

The first transfer involved fitting a frame to the cantilever beam to support the weight of the temporary services support. To insert the ITE, a temporary roller frame was located in the ITE bore and the ITE was rolled along the cantilever beam into position, where it was held to the rear support by means of a 4-peice CFRP ring. The load of the End-cap at the rear support was transferred to the beam using a yoke on the beam which hooked under the protruding “arms” of the rear support.

At the front of the End-cap, the gas and G&S membranes were attached and sealed (using Tempflex®), and the seals were made to the ITE at the inner radius of the membranes and the sides of the support cylinder at its outer radius. A temporary front support (TFS) made from invar was attached between the cantilever beam at the front of the support cylinder; the annular front stub support (FSS) had gaps exposing 10 of the 32 support fixing points on the support cylinder (5 on each side) for this operation. As the FSS and TFS used different fixing positions on the support cylinder, it meant the FSS could be removed, leaving the full End-cap mass on the cantilever beam.

Finally the assembly frame was carefully dismantled and the trolley was retracted, leaving the outer circumference of the End-cap clear of obstructions (see Fig. 43 and also Fig. 28) in readiness for the OTE, and later the TRT End-cap, to be slid over the SCT.

Fig. 43. Sketch showing the End-cap held solely on the cantilever beam.

The OTE was designed to be located on the rails fixed to the support cylinder. These rails were adjusted prior to mounting the OTE to match the actual inner diameter of the OTE. A simple table-mounted support was used to align coaxially the OTE and SCT EC assembly before sliding on the OTE – see Fig. 44. Once the OTE was in place, the tabs on the outer edge of the rear G&S membrane were bent over and soldered to the flange of the OTE. At the front, the front gas membrane was sealed to a flange on the inside of the OTE using Tempflex®, then the front G&S membrane was soldered to the OTE to complete the Faraday cage.

Fig. 44. OTE being added to one End-cap.

At this point, the End-cap was tested for leak-tightness and the remaining gaps were sealed with Tempflex®. Leak rates of 85 and 350 l/h at 1 mbar overpressure were achieved for EC-A and EC-C respectively.

## TRT Integration

To integrate the SCT and TRT End-caps, guide rails were accurately positioned in front of the SCT on the cantilever beam and the trolley carrying the TRT was placed onto these rails. The two detectors were then accurately aligned coaxially using the TRT trolley adjusters. To start the integration, the TRT was slowly pushed up to the SCT and the clearance gap between them checked in several places – there turned out to be slightly more than the nominal 6 mm minimum radial clearance. The TRT EC was then slowly pushed over the SCT. During this operation the alignment and clearance of the two detectors was continually monitored by observers situated around the assemblies – see Fig. 45.

Fig. 45. Integration of the TRT and SCT End-caps.

Once the TRT was fully integrated with the SCT, the bridge plate (see Fig. 46) was fastened to the 22 exposed fixing points on the support cylinder (11 upper and 11 lower points). The horizontal gap between the plate and the end of the support cylinder allowed access to the TFS fixings and allowed its removal. Subsequently, the front support was able to be inserted and bolted to the cylinder. The ITE was connected via a flange to the front support, and the roller frame, which was supporting the ITE up to this point, was removed. The support mechanism components (see Section 4.1.3) were added to the front support. These were shimmed to just rest on the TRT services support frame (the “squirrel cage”) taking the mass of the SCT assembly without changing the relative position of the SCT and TRT. The bridge plate was removed and the in-fill pieces (see Section 4.1.2) were added to cover the exposed sections of support cylinder.

Fig. 46. Bridge plate, used to support the front of the SCT End-cap at the top and bottom of the support cylinder.

The rear support mechanisms were attached to the ends of the rear support and again shimmed to just rest on the squirrel cage. The yoke supporting the rear support was released and removed, transferring the rear load of the SCT to the squirrel cage. Finally, the TRT trolley along with the SCT was retracted from the cantilever beam.

## Survey

The dowels in the support cylinder which define the orientation of the SCT (see 6.2) were surveyed in the End-cap relative to the temporary rails used for the integration with the TRT. By combining the information from the surveys, the target holder dimensions and the survey of the ID rails, it was possible to determine the transverse position and angle that each end of each End-cap would have when installed in ATLAS [39]. The End-caps were deliberately set about 1.5 mm low (negative y) because the solenoid field axis is known to be 2.5 mm low and the rails are expected to sag by 1 mm when loaded with the weight of the Inner Detector. It was necessary to re-adjust the End-cap positions with shims after the first survey in order to reach the final positions reported in Table 1.

|  | EC-A, D9 end | EC-A, D1 end | EC-C, D9 end | EC-C, D1 end |
| --- | --- | --- | --- | --- |
| x offset (mm) | 0.34 | 0.21 | 0.92 | 0.28 |
| y offset (mm) | 1.14 | 1.50 | 2.04 | 1.48 |
| Rotation (mrad) | 0.36 | 0.16 | 0.49 | 0.66 |

Tab. 8. Calculated x-y positions of the two ends of each End-cap when installed on the Inner Detector rails. Positions are relative to the IWV coordinate system and do not include the expected rail sag.

## Tests after Integration into the TRT

The performance of the SCT End-caps after integration into the TRT was studied in the SR1 surface building at CERN. Tab. 9 summarises the results of these studies for EC-A – more information will be available in a forthcoming paper on the commissioning of the SCT. The average number of dead channels at this stage was 3.21 (0.21%) per module, compared to 3.28 when measured after assembly at NIKHEF – some channels having been recovered.

| Problem | End-cap A |
| --- | --- |
| Inner module noise | 1121 ± 50 enc |
| Middle module noise | 1609 ± 70 enc |
| Outer modules noise | 1675 ± 75 enc |
| Dead channels | 3169 = 0.21%, no dead chips or modules |
| Problematic data links (each links serves half a module) | 27 – but can use other link to readout module, so no loss of functionality, only redundancy |
| Dead timing, trigger and control links | 1 – but due connections from nearest neighbours, no loss of functionality, only redundancy |
| Blocked/leaking cooling circuits | none |

Tab. 9. Snapshot of performance of End-cap A after integration in SR1.

Information from EC-C DERVAN

# Integration into ATLAS

Having integrated the SCT and TRT, the final phase of the engineering project was the transportation of the End-cap to ATLAS, the insertion into the cryostat and the connection of all the services.

## Transport and Insertion into ATLAS

The movement of the End-caps to ATLAS was more delicate that the transportation to CERN, since the SCT was now supported by the CFRP front and rear supports, as opposed to the more rigid stub supports (see Section 6.1). The maximum dynamic acceleration was specified to be less than 0.1g in the range 1 to 100 Hz and the maximum equivalent static acceleration to be smaller than 0.2g in any direction [37].

Clamps were mounted to restrain the support ends vertically and rigid bar supports were added to prevent longitudinal motion. Capacitive accelerometers were installed onto the SCT in the longitudinal and vertical direction in order to monitor the static accelerations. A tilt-meter was added to ensure that a maximum tilt of 1o about the horizontal axis was not exceeded. Each End-cap was placed in a wooden box and wheeled out of SR1, with rails over the uneven parts of floor. To move the End-cap the 100 m to the ATLAS service building, mobile cranes were used in order to minimise the shock.

Once inside the service building, the End-cap was lowered down the shaft using the service building cranes. In the pit, the End-cap was positioned on a cradle and rotated 90o to be inline with the cryostat bore. Then the End-cap trolley was moved on rails towards the cryostat bore. Having aligned the rails, the End-cap was inserted using a push-pull mechanism – see Fig. 47. This employed one drive and a worm-gear unit, to make sure that on both sides of the End-cap, the movements were equal and no shear was introduced. Wire length meters were used to monitor the difference in movement between the two sides. With the Inner Detector Barrel outside its envelope longitudinally and to prevent damaging the services of the Barrel, a thin copper sheets was placed between the Barrel and End-cap. This sheet was connected to an electrical circuit to detect when the assemblies would make contact and hence avoid additional forces which might lead to damage. In the case of the first End-cap, it made contact approximately 5 mm before its nominal position in z.

Fig. 47 Installation of EC-A into ATLAS.

## Installation of Services

The final step was the routing and connection of the SCT services at the PPF1 patch panels near the corner of the Cryostat – see Fig. 48. Tab. 10 summarises the services for each End-cap and the numbers and types of patch panels. A schematic of the PPF1 lay out is shown in Fig. 49. All the services from PPF1 to the racks were preinstalled and tested.

Fig. 48 Installing services in ATLAS.

| Services | Number | Patch Panel |
| --- | --- | --- |
| PPF1 housings and cable trays | 18 |  |
| LMT mono phase cooling loops | 16 | Divided over 8 electrical and 8 combined electrical and optical patch panels |
| Low-mass tapes (LMT) | 1976 |  |
| Readout optical ribbons | 178 | Divided over 8 combined electrical and optical patch panels |
| FSI optical ribbons | 45 | Run through 4 combined electrical and optical patch panels and spliced at PP2 |
| Heat exchanger assemblies | 36 | Divided over 4 cooling and 4 combined cooling and DCS patch panels |
| DCS cables | 40 | Divided over 4 combined cooling and DCS patch panels |
| Grounding and shielding clamps | 16 | Connected at 16 places on the radial cable tray (RCT) |
| Heater pad cables | 72 | Divided over 2 combined heater pad and nitrogen patch panels |
| Nitrogen tubes | 5 |  |

Tab. 10. Summary of the external SCT End-cap services and their patch panels (PPF1).

Fig. 49. Schematic showing the PPF1 patch panels.

Routing and connection of most services was done in layers, preventing access to the previous layer. After each installation step, testing was undertaken before the next layer was installed. The first step in the installation was the connection of the cryostat cable trays (CCT’s) and the Cu-polyimide shielding, followed by the LMT mono-phase C4F10 cooling loops. The cooling loops provide the cooling for the LMT’s outside the SCT and for the cables to which the LMT’s connect. The next step was the installation of the eight electrical PPF1 housings for LMT connections. At the same time, the FSI optical ribbons were routed to the splice box and the readout optical ribbons were installed in the combined electrical and optical patch panels. Following the installation of the PPF1 tray housings, the LMT’s were installed. Each quadrant has four PPF1 tray housings, with each housing holding nine trays, each tray being equipped with a maximum of nine LMT’s. Tests were performed in the electronics caverns, which house the power-supplies, using a standalone test system to measure the resistances of all the lines. Problems with the connections or cables were sorted out immediately and fixed before moving to the next layer. In total, 157 problems were registered with the LMT installation. Most of the problems were found to be bad connections at PPF1, incorrectly mapped cables and a few problems downstream of PPF1. One problem was found with an LMT shorted to ground, which was beyond repair. After the installation of each complete housing, the LMT’s were wrapped with aluminium foil together with the LMT mono-phase cooling loops, the cable tray lids weree added and the Cu-polyimide foils closed providing shielding for the PPF1.

All readout optical ribbons for one quadrant were installed prior to testing. The optical ribbons leaving a certain quadrant were connected to modules and hence LMT’s in the neighbouring quadrant. To test the modules in the absence of cooling, each module was powered for approximately just seven seconds to avoid over-heating. To test the readout optical ribbons, the PIN currents were measured and a super-fast RX threshold scan was performed.

Next, the heat exchanger (HEX) assemblies were installed (see Section 9). Originally the evaporative heaters should have been installed together with the HEX assemblies, but due to electrical problems with the heater connectors, it was decided to redesign the system and move the heaters to a more accessible position on the cryostat flange to allow for future maintenance. The HEX assemblies were connected to the connectors at the end of the on-cylinder cooling circuits at the point where they leave the End-cap. Specially made connectors were used with PEEK washers to make electrical breaks between the on-cylinder pipes and the HEX assembly. After leak-testing each circuit, feed-through boxes were added and sealed to close the End-cap thermal enclosure and all the pipes were insulated. To complete the cooling circuits, the so-called “near pipes” were installed, followed by the Heaters. These pipes connect the exhausts of the HEX’s with the heaters. After the completion of all the circuits in a quadrant, leak-tests of the complete evaporative lines were performed.

With all the services installed, the rear sections of the RCT were added to support the radial services. The final step in the installation was the leak-testing of the thermal enclosure volume, followed by the connection and testing of the DCS cables, heater pad cables and the nitrogen lines.

Fig. 50. Cooling system outside the End-cap – showing the heat-exchangers and heaters WERNEKE.

# Grounding and Shielding

## Concepts

The strategy for the grounding and shielding [40] is that all conductors not used for carrying currents to/from the detector must be connected by a low-impedance path to the cryostat, which in turn is connected to the ATLAS main ground. Where possible, loops are avoided to reduce the noise picked up on signal lines.

The End-cap module has a number of existing features to limit the stray capacitance of the detector backplane to the two cooling heat sinks. Primarily, the backplane AC referencing conductor is routed to a large bypass capacitor on the hybrid, which couples the backplane to the front-end analogue ground. The capacitor is of order ten times larger than the detector stray capacitance to the metallic cooling sink. The module is separated from the cooling block by electrically insulating thermal grease (DC340). In order to limit noise currents in the front-end, the cooling pipe DC-references to the module at the power-supply module entry region and a DC electrical connection from analogue ground on the module to the cooling tube is implemented (more details can be found in [40]).

To prevent the timing, trigger and control (TTC) redundancy links from generating excess noise in the front-ends, there are very low-impedance connections for the digital return signal from one module to its neighbour.

The modules are referenced to the cooling pipes on the disks while the hybrids are connected to the grounds on the power tapes. The pipes are connected to the grounding foils on the disks which in turn are connected to the ground sheet on the support cylinder. Likewise all the components inside the OTE are connected to the ground sheet (see Section 4.2), which provides the principle grounding path out of the End-cap to the radial cable tray (RCT).

To shield the front-end electronics from external pick-up noise, the End-cap is enclosed in a Faraday shield formed from the Cu-polyimide foil on the OTE and ITE and the front and rear membranes. This shield also connects to the RCT. Originally it had been hoped to use aluminium facesheets to reduce the number of radiation lengths; however because of the difficulties of making reliable low-resistance connections with aluminium, copper was chosen since this allows strong physical bonds of low resistance to be made very easily. Sheets of Cu-polyimide were connected using a “bridging” technique explained in Section 8.4.1 and illustrated in Fig. 51. To facilitate the handling of the copper foil strip (3 mm wide) used to form the “bridge”, the foil was cut into sections O(1) cm long and joints were made with O(1) cm gaps between each length of foil along the joint. At the services feedthrough (STFT), gaps allow services to pass through. As a rule of thumb, an attempt was made to limit apertures to less than 1 cm ×10 cm.

Fig. 51. “Bridging” technique for solder connection between two sheets of Cu-polyimide.

The RCT is electrically connected to the cryostat cable trays (CCT’s). To ensure good connections, the cable trays were treated with Alochrome 1200 and fingerstock was inserted in the gaps to ensure penetration of surface oxide layers. All services, including the monophase LMT cooling pipes are referenced to the CCT’s, which are connected in turn to the PPF1’s. Finally the PPF1’s are bolted to the segmented plate located at the flange of the cryostat – this plate is robustly connected to the main ATLAS ground. To avoid noise transmission from outside to the End-cap, the evaporative module cooling circuits are isolated at the STFT, while the monophase cooling is isolated in the vicinity of the PPF1’s.

## Measurements

To check the correct implementation of the grounding scheme, extensive measurements were made to ensure that intended connections were indeed of low resistances and no unwanted electrical paths had been created inadvertently. Measurements of various items used in the assembly of the two End-caps were done in a systematic way in the SR1 surface building at CERN so that any rectifications could be undertaken before the End-caps were installed in ATLAS.

Two measurement techniques were used:

- A standard multi-meter was used to measure resistance with a precision of 0.1-0.2 . Since a multi-meter functions with a very small voltage, this method presented a low risk for devices built with semiconductors.

- A current source set with a limit of 3A combined with a very precise voltage measurement enabled resistances to be determined down to 10  (impossible with the other technique). This method, unsuitable for sensitive devices, was used to ensure good connectivity for the outer Faraday shield, in particular the connections within and to the OTE and ITE.

The criteria used when checking the various connections were that conducting paths should have resistances less than 0.2  while insulating paths should have resistances in excess of 1 M.

The measurements were made at various stages of the End-Cap assembly in SR1. Following the reception of the End-caps from Liverpool and NIKHEF, it was found that pipe brackets on the support cylinder were floating, therefore connections to the ground sheet were made. Before integration with the End-cap, the OTE, ITE, shunt shields, front and rear support assemblies were subjected to a large number of measurements. The connectivity between the different sheets of Cu-polyimide (resulting from the bridging technique of previous section) within the OTE and ITE was much better than 1 m. However it was found to be necessary to add conductive tabs connected with conducting glue to ensure the electrical connectivity of the aluminise polyimide sheets. To ensure the isolation of the SCT from the TRT rails, the carbon-loaded PEEK inserts in the support mechanisms (see 4.1.3) had to be replaced by unloaded PEEK ones.

After the insertion of the End-cap C into ATLAS, a connection to the SCT Barrel was detected. By inserting an endoscope between the cryostat and the End-cap, it was found that the short was due to a CO2 pipe. The pipe was moved in situ and some insulation inserted.

# Status of the End-caps

From arrival at CERN to readiness to be installed in ATLAS took around one year.

## Status of the Hardware

At the time of writing, both End caps have had all their electrical and optical services connected. The electrical and optical connections for End-cap A have been checked but measurements of the module performance will only be done after all the cooling services have been installed. Simple functionality tests are being made to check that electrical and optical connections – these are undertaken by powering the modules for 10 seconds at a time, but do not allow analogue measurements.

Any updates ?

## Mass Estimates

It is important to estimate the mass of the detector to ensure that it conforms well to the expectations and does not exceed the limits calculated for the support structure. The original design estimate of the mass was 168 kg. It is calculated that 30% of the load is on the front supports, while the rest is on the rear supports. In the structural analysis, a safety factor of two was used for the material properties, and there was a further safety factor of at least 30% in the predicted stresses. After the support structure was manufactured, it was proof-tested to more than 1.5 of the original working load (277 kg of blankets were draped over the structure). After the front and rear supports were modified to take the survey targets, they were retested. The mass budget had increased, and so they were retested with a new load of 300 kg via a dummy structure bolted between the supports.

Furthermore, it is important to estimate the mass distributions accurately to understand the effects of multiple-scattering, nuclear interactions, bremsstrahlung and pair creation in the detector and to ensure the correct representation in the Monte Carlo simulation for physics studies. To ensure an accurate transfer of the energy scale from the Inner Detector to the Electromagnetic Calorimeter, it is desirable to understand the material distribution at the level of 1% (of its value). This is very challenging, although this is most critical at the inner radii. Components of the End-cap have been systematically weighed, although this has been harder for those components at higher radii, where significant amounts of Tempflex® sealant have been required, additional fastenings have been added and the masses of cables and their wrappings have been less easy to control. Nevertheless, the estimates for the disks before the addition of modules (which are well described themselves) from the bottom-up approach agree with the weighed values to 1.4%, and even then the simulated values are adjusted to reproduce the total weights. At the same time, care has been taken to understand the composition of the materials used to estimate correctly the radiation lengths. The estimates of the various components are given in Tab. 11. Distributions of the numbers of radiation lengths can be found in [41].

To verify the bottom-up estimates, the SCT End-cap weight was determined using load-cells to weigh the TRT End-cap in its support frame with and without the SCT. This measurement was undertaken before integrating the End-cap into ATLAS; hence most of the cable trays and PPF1 components were missing at this stage. The estimated mass was 174.2 kg, to be compared with the measured mass of 171.8 kg, with an error of the order 10 kg. These numbers correspond fairly closely to the mass which would be supported by the front and rear supports – this is estimated to be 175 kg and should be compared with the original design estimate of 168 kg (above).

| Components | Mass (kg) |
| --- | --- |
| Modules | 23.7 |
| Disks | 30.3 |
| Support cylinder and associated services and OTE | 57.4 |
| Other support structures (front and rear supports, ITE) | 22.8 |
| Services between STFT and cryostat, including RCT | 41.2 |
| Services on cryostat, including cryostat cable trays | 46.8 |
| PPF1’s | 34.5 |
| Total | 256.7 |

Tab. 11. Bottom-up estimates of masses of End-cap components.

## Expected Tracking Performance

The expected tracking performance for the Inner Detector is documented in [41]. When collision data has been collected, analysed and understood, more complete performance studies will be documented.

# Things To Do Differently

In designing the SCT End-cap, various decisions needed to be made. In retrospect, and in particular in the light of problems constructing the SCT, it might have been better to consider different approaches. In this section, some of these areas are highlighted; nevertheless, it is not obvious that there alternatives would necessarily be better.

## Layout

To improve the track parameter resolution and reduce correlations between the parameters, the stereo orientation alternated from disk to disk. This led to a large number of “flavours” of disks and their services. This made the design and assembly more complicated, requiring more drawings and the unit cost of components was higher. This configuration actually led to a design error for the Barrel power tapes.

The last disk, Disk 9, was rotated to place the silicon at the largest pseudorapidity. This complicated the design of the patch panels.

In general, it would be worth trying to keep all the disks as similar as possible to minimise design effort, cost and minimise the possibility for mistakes.

The modularity of 52, 40 and 40 modules for the outer, middle and inner rings arose from the desire to extract silicon detectors from round 4-inch wafers which maximised the use of the surface area and reduced the cost. This resulted in very many “flavours” of services being required, each of fairly complicated design. Some of the costs savings on silicon may have been lost in the complexity of the services and it is probable that the mass of services is greater than it might have been otherwise. It would be worth considering a design which had a much higher degree of rotation symmetry for the disks – the current design only has 4-fold rotation symmetry. It would be attractive to consider a “pointing” geometry with equal numbers of modules in each ring.

## Disk Services

Originally it was hoped to use aluminium cooling pipes with aluminium cooling blocks. The pipes would have been much easy to bend and the circuits could have had fewer radiation lengths. This solution was abandoned due to the difficulty of connecting the blocks to the pipes in a way which would not have created metallic joints with metals having large differences between their galvanic potentials, allowing the possibility of corrosion. It would be worth investigating all-aluminium welding or soft-soldering techniques to avoid this. Nevertheless, there is always a risk of corrosion arising further downstream at the junction between dissimilar metals. Unfortunately welding is expensive and tends to dissolve the aluminium.

Carbon-carbon was chosen for the cooling blocks. While this material potentially has good thermal conductivity in certain directions, the conductivity is variable and it proved difficult to envisage simple QA procedures to select good material. Furthermore, the material was quite difficult to machine because of its softness and intrinsic fault lines. The resultant blocks were quite delicate and prone to breakages during assembly to the pads on the disks.

Block positioning was a difficult and time consuming operation. The mounting screws had to be sufficiently tight to hold the block down onto the mounting pad and to overcome the natural flexibility of the pipe. The only item to grasp was the block rather than the thin walled pipe and there was only very restricted access under the optics. Since the precise placement of the blocks was critical process, it would have benefited from much more prototyping.

The design of the cooling circuits required a number of soldered joints to be made after mounting on the disks; this prevented testing prior to assembly. Consequently, it was impossible to obtain complete access to these joints for either soldering or for visual examination. The layout of the pipes, with both sides of the disk sharing common connectors, made it difficult and time consuming to find any leaks. Any leaks which were found meant that the cycle of cleaning and testing had to be repeated. This process denied any access for other installation operations which impacted on the timescales. These problems stress the importance of having completed, tested modular components which can be used in the assembly.

To reduce the possibility of corrosion at PPF0 due to the choice of aluminium seals (see Section 2.2.1) it would be desirable to use copper seals with sturdier housing in order to supply the required compression of the seals.

The FSI system proved to be very delicate and there was no way envisaged during assembly to check its integrity. The quartz rods in the jewels were chosen to reduce thermal distortions, however they were exceptionally fragile and prone to shattering. In retrospect, some other low-CTE material should have been chosen.

It was unfortunate that stress-relief for the cooling circuits required excessive bends adding to the material. While some consideration was given to circumferential cooling, this would benefit from further investigation.

Putting delicate fibres on the disks where they get damaged and cannot be replaced because they are under cooling circuits was a mistake. We now have a significant number of dead VCSEL’s on the disks and we must rely on the in-built redundancy to ensure that there is no loss of signal. It might be better to carry electrical signals from the modules to the edge of the disks and then convert to fibre. Due to the fragility and inaccessibility of the services, a large portion of the disk build-time was spent testing and re-testing services (maybe 30% prior to module mounting). Unfortunately the continual connection and re-connection at all the interfaces has increased the likelihood of failure. More thought should have been given to the overall testing regime: either to improve the accessibility of services, enabling them to be swapped more easily late in the process, or by making them all more robust, reducing the need for continual testing. A more robust design would use electrical connections from the modules to a nearby optoelectronic interface. This would avoid having fragile fibres on the disks and would allow the optoelectronics to be located in regions, such that they could be replaced more easily in the event of failures during assembly.

## Large Structures

The flexible gas and grounding-and-shielding membranes were conceptually simple and low mass. However, in the event of access being required to the insides of the End-cap, the membranes will undoubtedly be destroyed, requiring spares to be made. While the soldering technique for connecting the outside of the Faraday shield has proved very adaptable and straightforward, it is time consuming to seal or unseal the components. The use of copper adds to the number of radiation lengths – it would be worthwhile to investigate welding techniques for aluminium foil which could be used in situ without risk to the other components.

## Assembly

The concept for sealing the End-cap relied heavily on the application of Tempflex® and Techsil® sealants. These are messy and required in poorly defined amounts. Nevertheless, the approach was flexible and there is some inevitability that loose sealant will be required to block all sources of leaks.

There is a conflict between the requirements of building low-mass, thin-walled cooling circuits and the rigidity needed to provide firm seals. This would benefit from much greater investigation and every effort should be made to keep crucial connections outside relatively inaccessible regions: it is not good to have the connectors at the end of the cooling interconnects on the support cylinder buried inside the STFT.

A lot of effort went into designing low-mass cooling connectors. Several of the prototypes proved inadequate. Instead there is sense in using off-the-shelf connectors where ever possible.

# Conclusions

The engineering for the ATLAS SCT End-cap will have been completed by the end of 2007. It has been a large endeavour involving many engineers, technicians and physicists. The engineering, in particular that associated with services, is not very glamorous compared to the design of silicon detectors, and yet without it, the detectors cannot work. Furthermore the challenges involved in the engineering design and implementation have been as great as any other part of the experiment and collaborations forget this at their peril. It is all too easy to ignore the huge amounts of manpower, money and time in undertaking the engineering for a project of this scale and it is not made easier by all the external constraints which add greatly to the complexity, requiring components at the edge of what is technical realisable.

Despite the bright ideas of the ATLAS physicists, it is a credit to our engineers that this project has been successfully realised.

# Acknowledgements

The ATLAS SCT Collaboration would like to thank Mr. John Noviss as well as the technical staff at the following institutes: CERN, Glasgow University?, IFIC (Valencia), Lancaster University, Manchester University?, NIKHEF, Oxford University?, Queen Mary College (University of London), Sheffield University.

# References

ATLAS Engineering Documents can be obtained from:

https://edms.cern.ch/cedar/plsql/edmsatlas.home

ATLAS Notes can be obtained from:

http://cdsweb.cern.ch/collection/ATLAS

- The ATLAS Collaboration, Inner Detector Technical Design Report, 1997, Vol 2, CERN/LHCC/97-17.

- The ATLAS Collaboration, Magnet System Technical Design Report, 1997, Vol 1, CERN/LHCC/97-18.

- The ATLAS Collaboration, The ATLAS SemiConductor Tracker End-cap Module, 2007 Nucl. Instr. Meth. A575 353.

- The ATLAS Collaboration, Inner Detector Technical Design Report, 1997, Vol 1, CERN/LHCC/97-16.

- S. Haywood, Stereo Definitions for the SCT, 2002 ATLAS Engineering Document ATL-IS-ES-0077.

- N. Hessey, Physics Requirements for End-cap Module Placement Tolerances, 2001 ATLAS Engineering Document ATL-IS-ER-0027.

- S. Gibson et al., ATLAS SCT End-cap Alignment System Layout, 2005 ATLAS Engineering Document ATL-IS- ES-0081.

- P. Coe et al., Frequency scanning interferometry in ATLAS, 2004 Meas. Sci. Technol. 15 2175.

- S. Gibson et al., Coordinate measurement in 2-D and 3-D geometry using frequency scanning interferometry, 2005 Optics and Lasers in Engineering, 43 815.

- I. Dawson et al., Radioactivation of silicon tracker modules in high-luminosity hadron collider radiation environments, 2003 Nucl. Instr. Meth. A515 422.

- Paper in preparation.

- P. Werneke, Performance Requirements of Disks and Inserts, 2003 ATLAS Engineering Document ATL-IS- ES-0041.

- N. Hessey, P. Werneke, Choice of Korex® material for the next NIKHEF disk prototype, 2001 ATLAS Engineering Document ATL-IS- ER-0029.

- N. Hessey et al., SCT End-cap Disc Preparation for Services, 2001 ATLAS Engineering Document ATL-IS- AN-0003.

- S. Haywood, XY Metrology of SCT End-cap Disc 9C, 2003 ATLAS Engineering Document ATL-IS- ER-0051.

- Q. Snippe., Structural Analysis of the End-cap Discs, 2003 ATLAS Engineering Document ATL-IS- EA-0004.

- I. Wilmut et al., SCT End-cap Disc Services Design, 2003 ATLAS Engineering Document ATL-IS-ER-0016.

- R. Fowler, CFD Simulations of Convective Heat Transfer in the ATLAS SCT End-cap, 2001 ATLAS Engineering Document ATL-IS-ER-00020.

- CFX 4.2 User Manuals, CFX International, Harwell, Didcot, UK (1997).

- I. Duerdoth et al., Measurements of Convection between the Disks of the SCT End-cap, 2004 ATLAS Engineering Document ATL-IS-TR-0010.

- V. O’Shea, SCT Forward Power Tape from PPF0 to Module, 2003 ATLAS Engineering Document ATL-IS- ES-0082.

- A. Abdesselam et al., The Optical Links of the ATLAS SemiConductor Tracker, 2007 The Journal of Instrumentation 2007_JINST_2_P09003.

- P. Philips, Functional Testing of the ATLAS SCT Barrels, 2007 Nucl. Instr. Meth. A570 230.

- J. Bohm et. al., Power supply and power distribution system for the ATLAS silicon strip detectors, 2001 CERN-2001-005.

- M. Chu et al., Optical Links of the ATLAS SemiConductor Tracker and Pixel Detector, 2004 Nucl. Instr. Meth. A530 293.

- J. Butterworth et al., TIM (TTC interface module) for ATLAS SCT and pixel readout electronics, 2001 CERN-2001-005.

- J. Tarrant et al., SCT End-cap Support Structure, 2001 ATLAS Engineering Document ATL-IS- ER-0017.

- C. Nelson, FE Analysis of SCT End-cap Support Structure, 2001 ATLAS Engineering Document ATL-IS- EA-0001.

- C. Nelson, SCT End-cap Support Structure – Frequency Response Analysis, 2001 ATLAS Engineering Document ATL-IS- EA-0002.

- V. Juraylev et al., Investigations of Power and Spatial Correlation Characteristics of Seismic Vibrations in the CERN LEP Tunnel for Linear Collider Studies, 1993 CERN Report CERN-SL-93-53.

- A. Weidberg, proceedings of LECC (Heidelberg) 2005.

- S. Haywood, Transportation for the ATLAS SCT End-cap (EC-C), 2005 ATLAS Engineering Document ATL-IS- CS-0016.

- J. Tarrant et al., SCT End-cap Thermal Enclosures, 2004 ATLAS Engineering Document ATL-IS-ER-0018.

- F. Hartjes, Moisture management in the ATLAS SCT and Pixel Tracker Using Dry Nitrogen Flow, 2003 ATLAS Engineering Document ATL-IS-EN-0015.

- P. Ford, SCT End-cap Thermal Enclosure Post-FDR Prototyping and Analysis, 2005 ATLAS Engineering Document ATL-IS-ER-0058.

- P. Ford, Heat Transfer Analysis of the Thermal Enclosure, 2004 ATLAS Engineering Document ATL-IS-EA-0006.

- P. Werneke and J. Tarrant, Transport of the SCT End-cap from SR1 to the ATLAS Pit, 2007 ATLAS Engineering Document ATL-IS-ES-0117.

- B. Smith, SCT End-cap Integration Procedure, 2005 ATLAS Engineering Document ATL-IS-ER-0067.

- J. Foster et al., SCT Endcap Geometry and Surveys, ATLAS Note ATL-INDET-PUB-2007-004.

- S. Haywood et al., ATLAS SCT End-cap Grounding and Shielding, 2007 ATLAS Engineering Document ATL-IS-EN-0014.

- The ATLAS Collaboration, The ATLAS Experiment at the CERN Large Hadron Collider, to be submitted to The Journal of Instrumentation.

# Footnotes

YSH-50A/RS-3, supplied by YLA Inc.

Korex-5/32-2.4, supplied by Hexcel Composites.

Also made of YSH-50A/RS-3.

RS4, supplied by YLA Inc..

T500, supplied by YLA Inc..

Castolin 197, 70:30 lead-tin.

Supplied by Dunlop.

Conical washer, capable of providing a small spring force.

DC340 manufactured by Dow Corning.

Helicoflex® HN120 and HN100 seals manufactured by Garlock Sealing Technologies.

Swansolve ionic cleaner, supplied by Swan Tek.

Specification IPCC 2221.

Samtec FTM-114-03-L-DV and CLP-115-02-L-DV.

Yellow furcation tubing had been tested; however, this was transparent to infra-red light and therefore useless.

The design of the “wiggly” circuits permitted easy movement of the blocks of the order of 1 mm.

YSH-50A graphite fibres in an RS-3 cyanate-ester resin matrix supplied by YLA Inc..

Korex®-5/32-2.4 supplied by Hexcel Composites.

RS4 cyanate-ester adhesive film supplied by YLA Inc..

FM73U manufactured by Cytec.

SynSpand 9899.1CF supplied by Loctite Aero.

T300/RS-3 plain weave, supplied by YLA Inc.

Supplied by Sheldahl

T300 plain weave fabric in an RS3 cyanate-ester resin matrix.

A trademark of SASIP Inc and supplied by ANSYS Inc.

Espanex®

Supplied by Enidine Gmbh.

Shockwatch shocklog micro accelerometers, supplied by Lamerholm Electronics Ltd.

Airex® R82.60 foam manufactured by Alcan.

The diameter of the CFRP cylinder was defined by the diameter of the mandrel during the autoclaving process. By design, this corresponded to the nominal diameter, and due to thermal expansion, was larger than the room-temperature value.

Corresponding to an aluminium foil outer facesheet rather than Cu-polyimide.

Inner Warm Vessel – the inner wall of the cryostat containing the solenoid.

Located in the crack between the barrel and end-cap calorimeters.

Supplied by Laird Technologies.

Using a Keithly 2010 instrument.

This is not quite true for the cooling circuits for the outer modules.

# Text boxes

Rear Support     STFT     Rear Thermal Pad     OTE     ITE     Front Support

Modules:

Short Middle   Inner   Middle   Outer

Rear Membrane  OTE Heater Pad  Front Gas Membrane  Front G&S Membrane

Disk screw

Cylinder fixings

Cu-Be spring